HIDROLOŠKE OSNOVE PLANIRANJA I UPRAVLJANJA AKUMULACIJAMA -

PRIMJER AKUMULACIJE BOLJUNČICA U ISTRI

SAŽETAK:

Akumulacije su najznačajniji vodnogospodarski objekti za vremensku i prostornu raspodjelu voda. Jedan od najvažnijih ulaznih podataka pri planiranju ili analizi njihova rada su hidrološke podloge o elementima vodne bilance. U radu je na primjeru postojeće akumulacije Boljunčica provedena analiza bilance dotoka u akumulaciju metodom generiranih vremenskih serija, kao i analiza gubitaka vode na poniranje. Radi se o akumulaciji izgrađenoj u krškom području, koja zbog prisutnih gubitaka vode nikad nije zadovoljila planiranu višenamjensku funkciju osiguranja vodnih zaliha za navodnjavanje. Za generiranje serija dotoka u akumulaciju upotrijebljen je autoregresijski Thomas-Fieringov model. Simulacijske su analize provedene matematičkim modelom SYMAC razvijenim upravo za potrebe tih obrada. Provedene su i statističke obrade rezultata provedenih simulacija povijesne i sintetičkih vremenskih serija dotoka.

Master thesis

HYDROLOGICAL ASPECTS OF PLANNING AND MANAGING WITH ACCUMULATIONS -

THE EXAMPLE OF BOLJUNČICA ACCUMULATION IN ISTRIA

# SUMMARY:

Accumulations are the most important water managing constructions designed for time and spatial distribution of water. One of the most important input data for planning or analyzing of their work, are hydrological data of water balance elements. Present work, on the example of Boljunčica accumulation analyzes inflow balance into the accumulation using generated time series method and water losses balance through sinking. Boljunčica accumulation has been constructed on the karst ground and, because of water losses, it’s multipurpose use espetially for irrigation has never been achieved. Autoregression Thomas-Fiering model for generating series of inflows to the accumulation has been used. Simulations have been performed by SYMAC mathematical model developed exclusively for this analysis. Statistical analyzes of results of   simulations  performed with real and generated time series of inflows have also been performed.