| 4th International Congress of Croatian Society of Mechanics September, 18-20, 2003 Bizovac, Croatia |  |
| --- | --- |
| ON THE STRESS DISTRIBUTION IN THIN-WALLED BEAMS |
| SUBJECTED TO BENDING WITH INFLUENCE OF SHEAR |
| Radoslav Pavazza and Branko Blagojević |
| Keywords: | Thin-walled beams, bending, influence of shear, stresses |
| 1. Introduction |

The ordinary theories of thin-walled beams assume that cross-sections remain plane during transverse bending. These theories are restricted to relatively long beams, where warping of the cross-section due to shear can be neglected. The theories can be applied in the analysis of relatively short beams, where the shear effect cannot be neglected, by taking into account deformation due to shear. Equations that consider this effect are known as Timoshenko’s equations (1(.

Considerable attention in the past is received to determine the shear factor, by which the deflection due to shear is defined. In the Timoshenko’s equations this factor is given as the ratio between the effective shear area and total area of the cross-section (or between the total area and shear area). Thus, it is dependent on the shape of the cross-section only.

The recent definitions of the shear factor, includes the Poison’s effect. This effect gives for the shear factor two to ten per cent greater values (or lower values) (2, 3, 4(.

In this paper, the shear factor will be assumed as a pure geometrical property. The analytical solution for stress distributions will be investigated. The cross-sections with the general shape will be considered. Some solutions of the problem can be found in literature, for simple rectangular cross-sections (5( as well as for simple thin-walled cross-sections with one axis of symmetry (6(.

2. Stresses in thin-walled beams subjected to bending with influence of shear

2.1 Strains and displacements

Assuming that the contours of the cross-sections of thin-walled beams with open cross-section maintain their shape it may be written (Fig1.)

where and are the displacements of an arbitrary point S of the cross-section contour in y and z-directions, and are rectangular coordinates, and are coordinates of an arbitrary pole P, s is the curvilinear coordinate of the point S from the starting point M, and are displacements of the pole P in y and z-directions, i.e. displacements of the cross-section contour as rigid contour, and  is angular displacement of the contour as a rigid contour with respect to the pole P;

whereis displacement of the point S in the -direction, is the rectangular coordinate system with respect to the point S, is the angle between the tangent  and the axis y and Oxyz is the rectangular coordinate system. By substituting  into , it may be written

,

,  ,  ,  ;

is the sectorial coordinate with respect to the pole P and the point M.

Figure 1. Displacements of an arbitrary point of the cross-section contour

The relation between displacements and the shear strain can be expressed as

.

Then, after substitution of

;

,    ,    ;,    ,   ;

is longitudinal displacement of the point , where, i.e. displacements of the cross-section contour in longitudinal direction as a rigid contour, and are the integration constants

;

, and are the components of the shear strain in the middle surface, with respect to the displacements, and, respectively;

;

,   ,  ;

and are the angular displacements of the cross-section contour as a rigid contour with respect to y and z-axis, respectively, is the relative angular displacement of the cross-section contour as a rigid contour with respect to the pole P. The strain in the longitudinal direction can be expressed as:

.

2.2 Stresses in terms of displacements

By ignoring the normal stresses in the cross-section contour direction, the Hooke’s low for the state of plane stress can be written as follows

,    ,

where is the normal stress in the longitudinal direction and is the shear stress in the beam middle surface, E is the modulus of elasticity and G is the shear modulus.

Thus

;

, and are the components of the shear stress with respect to displacements, and, respectively.

For the equilibrium of a portion of the beam wall in the longitudinal direction, it can be written

,

where is the wall thickness. If

,    ,

taking into account and , it may be written

;

,  ,   ,   ,   .

,  and  are the shear flows where,  and, respectively. This can also be written as follows:

;

,   ,   ,   ,   ;

is the cut-off portion of the cross-section area with respect to the coordinate s, i.e., and are static moments of the cut-off portions of cross-section area with respect to the z and y-axes, is the sectorial static moment of the cut-off portions of the cross-section area. Here, taking into account  and :

,    , ,   .

2.3 Equlibirium equations

It is assumed that the beam is loaded by transverse forces per unit length and  that pass through the shear axis, parallel to the x-axis through the pole P,

,    ,

where and are the surface loads with respect to the y and z-axes.

For a portion of the beam wall the following equilibrium equations can be written (Fig. 2)

,,,

.

Taking into account , this can be written as follows

,    ,    ,    .

By integrating by parts, this may further be written as

, ,	.

Figure 2. Equilibrium of a portion of the beam wall

By substituting (14) and (18) the following equations can then be written

;

,   ,   ,  ,   ,   ,

,  ,   ,  ;

,   ,   ;    ,   ,   .

If y, z and are the principal coordinates,

,  ,  , ,  =0, S( =0

then equations (27) take the form

,    ,    ,    .

2.4 Internal forces and shear stresses

Integration of the shear stresses over the cross-sections gives

,    ,    ,

where and  are the shear forces with respect to y and z-axis, respectively, and  is the moment of torsion with respect to P. Substitution of (20) into  gives

,    ,    .

Here,,,and integrating by parts:

, , ;, , ; , , ; , , .

Referring to  and  the following relations can be written

,      .

2.5 Shear stresses in terms of internal forces

By substituting  into , the shear stresses can finally be written as

;    ,   ,    .

2.6 Internal forces and normal stresses

By integrating the normal stresses over the cross-sections one may write

,   ,   ,   ,

whereand are the bending moments with respect to y and z-axes and B is the bimoment. By substituting (14) into (36), it may be written

, , ,

;

,   ,   ,

,    	;   ,

,    .

Substitution of  into  yields

,    ,    ,

,	    ,    ,

,

Integrating by parts, it follows

,    ,    ;

,    ,

,

, ,  ,.

Here

,    ,    ,

,    ;    ,

.

The second and third equations of , taking into account  and , can be written as follows

,

,  ;  ,

,   ,  ,

Here Ary, and Ar,yz are the cross-section shear areas with respect to  displacements, Arz, Ar,zy are the cross-section shear areas with respect to  displacements; (y, (yz and (z, (zy are the corresponding shear factors.

2.7 Normal stresses in terms of internal forces

By substituting  into , taking into account  and  it may be written

2.8 Cross-sections with one axis of symmetry

In the case of the cross-sections with one axis of symmetry (for example, z-axis)

.

where due to the symmetry, ,.

2.9 Cross-sections with two axes of symmetry

In the case of the cross-sections with two axes of symmetry

.

where due to the symmetry, , , ,

3. Illustrative example

Static moments of the cut-off portions of the cross-section area of the I-section are (Fig. 3)

, ,;

,  ,   ;

,  ,;

,  ,    ,

where due to simplicity  and  are denoted as  and;

,   ,  ,   ,  ;

;

,  ,  ;     ,

,  .

Figure 3. a) I-section section with curvilinear coordinates; b) static moment of the cut-off portions of the cross-section area; c) cut-off portions of the cross-section area

For a T-section,  (,). Thus

, ,    ,   ,

where. For bending in the vertical plane the normal stresses given by , taking into account  and , may be written as

,    ;

, ,  .

For, ,  ():

,  ;,.

Thus; and, for;

and   for.

For a simply supported beam under uniformly distributed transverse load, ,:

;,  ;,  ,

where l is the beam length. Thus, for and, respectively:

,    ;

.  .

4. Comparison with finite element method

The beam is modelled by quadrilateral membrane elements; the case  by 1440 elements, and the case  by 1536 elements; and.

Table 1. Comparison of the results of the analytic solution and FEA

|  | FEA | FEA |
| --- | --- | --- |
| h/l=1/5 | 1,047 1,045 0,2 | 1,047 1,046 0,1 |
| h/l=1/3 | 1,131 1,145 1,2 | 1,130 1,135 0,4 |

Here  and .

5. Conclusion

The stress distributions for bending with influence of shear of thin-walled beams are obtained in the analytical closed form. The expressions for the stress distributions are approximate; it is assumed that normal stresses in the transverse direction are small compared to the normal stresses in the longitudinal direction. The shear factor is determined as a pure geometrical property. The expressions are obtained for the beams with general thin-walled cross-sections.

The comparison with the results of the finite element analysis of a thin-walled beam with T-section subjected to uniform transverse loads has shown a high agreement of the obtained results.

References

Timoshenko, S. P., “On the correction for shear of the differential equation for transverse vibrations of prismatic bars”, Philosophical Magazine, Vol. 41, 1921, pp 744-746.

Cowper, G. R., “The shear coefficient in Timoshenko’s beam theory”, Journal of Applied Mechanics, Vol. 33, 1966, pp 335-340.

Bhat, U. and de Oliveira, J. G., “A formulation for the shear coefficient of thin-walled prismatic beams”, Journal of Ship Research, Vol. 29, No. 1, 1985, pp 51-58.

Senjanović, I. and Fan, Y., “The bending coefficients of thin-walled girders”, Thin-Walled structures, Vol. 10, 1990, 31-57.

Gastev, “Kratkij kurs soprotivlenija materialov”, Gosuizdat, Moskva 1959.

Boytzov G. V., “Analysis of the transverse strength of large tankers”, Sudostroenie, Vol.9, 1972, pp.17-23 (in Russian)

Radoslav Pavazza, prof.

Faculty of Electrical Engineering, Mechanical Engineering and Naval Architecture, University of Split, Ruđera Boškovića bb, 21000 Split, Croatia, E-mail address: radoslav.pavazza@fesb.hr

Branko Blagojević, assis.

Faculty of Electrical Engineering, Mechanical Engineering and Naval Architecture, University of Split, Ruđera Boškovića bb, 21000 Split, Croatia, E-mail address: branko.blagojevic@fesb.hr