LOW TEMPERATURE RAMAN STUDY OF BIS(TRIMETHYLSILYL)ACETYLENE

V. Mohaček-Grošev, K. Furić

Ruđer Bošković Institute, Bijenička c. 54, 10002 Zagreb, CROATIA

mohacek@irb.hr

Low temperature Raman spectra of a known catalyst bis(trimethylsilyl)acetylene (BTMSAC) were recorded  in temperature interval from 323 K to 10 K.  Below melting point which occurs at  276 K BTMSAC crystallizes in P21/c space group with Z=2.  Altogether  six phonons are expected below 100 cm-1, together with two internal modes linear angle bending at 40 cm-1 and Si(CH3)3 torsion which is practically free in liquid, but hindered in polycrystalline state [1]. Above 100 cm-1 there is a degenerate linear bending mode at 127 cm-1, three modes (SiC3 sym. def. mode, CH3 torsion A and B type [1], and CH3 sym. torsion) at 175 cm-1, three internal modes at 216 cm-1 (two SiC3 deformation, and one degenerate CH3 torsion). It is interesting to note that the triple stretching vibration occuring at 2108 cm-1 is asymmetric in crystalline state, the low wavenumber side of the bandwidth being considerably larger than the high wavenumber part of the asymmetrically constructed Lorentzian [2].

Fig. 1: Low frequency Raman spectra of BTMSAC at low temperatures. Laser plasma lines are marked with asterisks. Asterix in brackets denotes a coincidence of a plasma line and a BTMSAC band.

| [1] | V. A. Sipachev, L. S. Khaikin, O. E. Grikina, V. S. Nikitin, M. Traetteberg: J. Mol. Struct. 523 (2000) 1-22. |
| --- | --- |
| [2] | V. Mohaček-Grošev, K. Furić: Fizika A 14 (2005) 219-224. |