PARAMETERS OF INLAND WATERWAYS
-APPLICATION FOR SAVA COMMISSION

Prof. Marko Pršić, PhD C.E.

Dalibor Carević B.C.E.

Eva Ocvirk, MS. C.E.

University of Zagreb - Faculty of Civil Engineering, Kačićeva 26, 10000 Zagreb, CROATIA

tel: +385::1: 4639222,   fax +385::1:4639260, Email: car@grad.hr

Abstract

The «Sava basin initiative» is an international programme for the integral management of the Sava river basin. The member countries are Bosnia and Herzegovina, Croatia, Slovenia, Serbia and Montenegro. The new UN/ECE « Classification of European navigable inland waterways» covering 7 classes was created and accepted in1992. A bit earlier in 1992 the classification was adopted at the CEMT conference. It is based on the UN/ECE classification from 1960 and CEMT classification from 1961 that encompassed 6 classes. The UN/ECE classification from 1960 was created as a recommendation, and the UN/ECE classification from 1992 is a component of the European treaty -AGN from 1996 and therefore it obliges the signatory countries. Only the Republic of Croatia as a member of the Sava initiative signed the AGN. Other Sava initiative members announced to join soon. The UN/ECE '60 classification for the tugged convoy contained detailed parameters of the navigable way. The new UN/ECE '92 classification contains only the sizes of tugged convoys. The directions are given to calculate detailed parameters of a navigable way for the area of the «Sava basin initiative». A table of all detailed parameters for all the classes of a navigable way should be created on the basis of the given directions.

1 Introduction

The paper deals with standardization of detailed class parameters of inland waterways resulting from the main parameters of UN/ECE classification [2] from 1992 for the «Sava initiative» programme. The standardization should enable an easier application of the 1992 classification on the common waterways and their tributaries. The detailed parameters should contribute to the preparation of development plans.

The new UN/ECE classification [2] from 1992 does not contain detailed parameters of European navigable waterways. They should be handled separately due to respective differences in morphology and traffic. Detailed parameters are to be defined according to specific features. The paper focuses on the overall elaboration of detailed parameters within the Sava initiative. It encompasses two major waterways of different international classes: those of Sava and Danube, their tributaries of regional classes that are navigable on a short section around the mouth. The generalization is possible as there are only few navigable watercourses, and no considerable differences take place.

2 Navigation in the inland waterways

2.1 Standard vessels and convoys

Standard vessels and convoys that are going to be used are defined in the UN/ECE classification from 1992 [2,5]. The international class of a navigable waterway is secured by the vessels of the navigable waterway of the IV. class, with dimensions 85×9,5×2,5 [m], or of the larger size  (Annex IIIa).

2.2 Determination of the minimal radiuses according to classes of navigable waterways

The minimal radiuses for this classification have been adopted on the base of data analyses on minimal radiuses of the navigable waterways in the bends of the existing waterways and in several recommendations [1, 2, 7, 9, 10]. They are given in the shape of comparative graph of the adopted minimal radiuses within the «Sava initiative» and UN/ECE classification, Fig. 1.

3 Detailed parameters of the inland waterway classes for the "Sava initiative" programme

3.1 The width of the waterway in the direction

The widths of the navigable riverbed for the two-way navigation in direction for all the navigable waterway classes are determined by the analyses of disposable theretical and practical methods. The width structure of the two-way navigable riverbed in the direction in the standard overtaking operation of the downstream navigation is the following :

BF,r [m] = Br + 2×SS = (2,5×b + 2×tan 3( × lmax) + 2×0,5b =

= 3,5×b + 2×tan 3( × lmax = 3,5×b + 0,1 × lmax				(1)

and for the canal:

BF,k [m] = Bk + 2×SS = (2×b + 2×tan 1,5( × lmax + 2) + 2×1,5 =

= 2×b + 2×tan 1,5( × lmax + 5 = 2×b + 0,05 × lmax + 5			(2)

For the horizontal reserve "SS" between the navigable  gabarit  and watercourse profile the following is adopted in this classification:

SS=0,5×b	for rivers

SS [m]=1,5m	for canals.

where:

b 	[m]	- is the width of the standard cargo vessel, or the stiff tugged convoy (when the convoy is larger than a vessel)

lmax	[m]	- is the length of the standard vessel or stiff pushed convoy for the calculation of the navigable riverbed width

SB	[m]	- is the horizontal reserve between two navigable tracks

SS        [m]	- is the horizontal reserve between navigable gabarit and watercourse profile

Br	[m]	- is the width of the two-way navigable gabarit on the river in the direction in overtaking of the downstream navigation

Bk	[m]	- is the width of the navigable gabarit on the canal in the direction at   passing by

BF,r	[m]	- is the width of the two-way navigable riverbed in the direction on the navigable river

BF,k	[m]	-  is the width of the two-way navigable riverbed in the direction on the navigable canal

Fig. 1: The comparison of the minimal radiuses of the navigable riverbed in the bend according to the UN/ECE classification from 1960. and UN/ECE classification from 1992 (''the Sava initiative'').

|  |  | IV | Va | Vb |
| --- | --- | --- | --- | --- |
|  | Distance between tracks (m) | 2,0 | 2,0 | 2,0 |
|  | Distance to the brim (m) | 1,5 | 1,5 | 1,5 |
|  | Distance to the brim (m) | 1,5 | 1,5 | 1,5 |
|  | Upstream track (m) | 11,7 | 14,3 | 16,2 |
|  | Downstream track (m) | 11,7 | 14,3 | 16,2 |
|  | Total (m) | 28,5 | 34,0 | 37,5 |

Fig. 2	Diagram of the final parameter recommendations for the canal navigable riverbed width in the direction, for the IV and V navigable waterway classes.

The only exception is the class VIa on the river where the size of the horizontal reserve  between two navigable tracks in the direction will be calculated according to the expression: SS=0,5×b, but for "b" the width of the vessel, and not the convoy width will be taken.

The following general conditions were endorsed in this case:- The width of the standard stiff rigid convoy and the width of the standard vessel for the calculation of the navigable riverbed width are defined by the UN/ECE classification [5];- The hydrodynamics of the navigation considerably depends on the narrowness of the navigable riverbed defined by the ratio of the cross sections  "n". With the newer and future canals it ranges between  n=5,4 and n=6,3, and tends to the optimal value of  7;- The navigation dynamics in the horizontal plane is similar with that of canals and canalized rivers, and is different with rapid rivers, as the canals and canalized rivers  contain "still water";- The standard operation: overtaking in the downstream navigation on the rivers and passing by on the canals;- Standard horizontal winding angle  that defines the navigable track width in the direction is  : 1 =1,5  for the case of upstream river navigation and  passing by on the canal, and 2=3 for the case of downstream river navigation and overtaking on the canal;- The standard horizontal reserve size between two navigable tracks in the direction amounts: SB=0,5×b for rivers and SB=2 [m] for canals;- Standard horizontal reserve "SS" between the navigable gabarit and watercourse profile in this classification are adopted as:  SS=0,5×b for rivers and  SS [m]=1,5 [m] for canals.

3.2 The navigable waterway width in the bend

For I-III on the river

|  |  | IV | Va | Vb | Via | VIb | VIc | VII |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Distance between tracks (m) | 4,75 | 5,7 | 5,7 | 11,4 | 11,4 | 16,5 | 17,1 |
|  | Distance to the brim (m) | 4,75 | 5,7 | 5,7 | 11,4 | 11,4 | 16,5 | 17,1 |
|  | Distance to the brim (m) | 4,75 | 5,7 | 5,7 | 11,4 | 11,4 | 16,5 | 17,1 |
|  | Upstream track (m) | 14,0 | 17,2 | 21,1 | 28,6 | 33,0 | 43,2 | 49,1 |
|  | Downstream track (m) | 14,0 | 17,2 | 21,1 | 28,6 | 33,0 | 43,2 | 49,1 |
|  | Total (m) | 45 | 55 | 65 | 80 | 105 | 140 | 155 |

Fig. 3 Diagram of the final parameter recommendations for the natural and trained rivers in the direction from IV to VII class

It refers to rapid and canalized rivers I. - III. class with predominant tugged and self-propelled technology. As there are no canals from I. to III. class, neither expected in future, the navigable riverbed width is determined only for rivers in the bend on the  rapid and canalized river and is expressed by:

(3)

where:

b [m]		- is the width of the vessel, or the stiff convoy

lmax [m]	- is the length of the tugged convoy or self-propelled vehicle

R [m]		- is the radius of the navigable riverbed ax

For  IV. - VII. class on the river

It refers to rapid and canalized rivers IV. - VII. class with  predominant pushing technology. The expression for the final width of the navigable riverbed in the bend is :

(4)

where:		Ri,1[m]		- is the radius of the inner brim (closer to the center of curvature) of the navigable track B1 for upstream navigation on the rapid and canalized river on the concave (depressed) bank curve,

Ri,2[m]		- is the radius of the inner brim (closer to the center of curvature) of the navigable track B2 for downstream navigation on the rapid and canalized river on the convex (protruding) bank curve.

lmax [m]	- is the length of the stiff pushed convoy

2 []		- is the horizontal angle of  the  swerve of the vessel or the stiff pushed convoy, in the bend for the downstream navigation on the rapid river at the convex (sticking out) bank curve,

1 []		- is the horizontal angle of  the  swerve of the vessel or the stiff pushed convoy, in the bend for the upstream navigation on the rapid river at the concave (depressed) bank curve.

b [m]		- is the width of the vessel or stiff pushed convoy (when the convoy is larger than a vessel).

|  |  | IV | Va | Vb | Via | VIb | VIc | VII |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Distance between tracks (m) | 4,75 | 5,7 | 5,7 | 11,4 | 11,4 | 16,5 | 17,1 |
|  | Distance to the brim (m) | 4,75 | 5,7 | 5,7 | 11,4 | 11,4 | 16,5 | 17,1 |
|  | Distance to the brim (m) | 4,75 | 5,7 | 5,7 | 11,4 | 11,4 | 16,5 | 17,1 |
|  | Upstream track (m) | 20,0 | 26,0 | 33,0 | 34,0 | 41,0 | 48,0 | 54,0 |
|  | Downstream track (m) | 38,0 | 46,0 | 43,0 | 42,0 | 46,0 | 52,0 | 57,0 |
|  | Total (m) | 72 | 89 | 93 | 93 | 121 | 149 | 162 |

Fig. 4 Diagram of the final parameters recommendations for the navigable waterway width in the bend on the trained rivers, for the IV, V, VI and VII navigable waterway class.

For any navigable way class the procedure of width detremination of the navigable riverbed in the bend  by means of the expression above is iterative.

In this case the following conditions are decisive: - the decisive operation: passing by on both the rivers and canals:- Decisive swerve angle  for the calculation of the navigable river track width in the bend: 1 for the case of upstream river navigation and 2 for the case of downstream river navigation, is to be read off in dependence of the radius Ri of the inner (closer to the curvature center) brim of the navigable track in the bend and central angle of the navigable riverbed in the bend =30 [], from the Graewe 's  experimental diagrams  -  [8] that were worked out for the stiff pushed convoy  2xE1+ pusher. For the case of  passing by on the canal, the horizontal swerve angle 1, decisive for the calculation of the navigable river track width in the bend, is expressed in the dependence on the navigable riverbed ax radius and central curve angle =30 [] from the Graewe' s experimental diagram [8]. The decisive horizontal reserve size between two navigable tracks in the bend is: SB=0,5×b for rivers and  SB=2m for canals;- The decisive horizontal reserves  "SS" between the navigable gabarit and the watercourse profile in this classification are adopted as : SS=0,5×b for rivers and SS [m]=1,5m for canals.

3.4 The navigable channel depth

The needed navigable riverbed depth  on both canals and natural rivers is determined by: draught of the vessel, longitudinal vessel trim, vessel speed sink, absolute reserves (water cushion between the vessel bed and the navigable way bed) and inexatness of measurements, or the cut of the transversal cross section of the navigable way. [3RICHTLINIEN]:

T = Tv +  +  = t + t + Sz +  +  = t + C						(5)

where:		Tv [m]	-  is a navigable gabarit depth

t [m]	- is a draught of a vessel

t [m]	- is a longitudinal trim of a vessel

Sz [m]	- is a speed sink

 [m] 	- is an absolute reserve

 [m]	- denotes an imprecision of a measurement or a cut of a navigable way cross section

C [m]	- is a water depth below a keel - clearance.

The following general conditions were decisive:- For the depth calculation of a navigable riverbed the regional navigable waterways should secure the draught lower than up to 2,5 [m], the existing international the least of 2,5 [m], and the future international at least 2,8 [m] [2 and 5];- The navigation dynamics in the vertical plane significantly depends on the tightness of the navigable way transversal cross section; consequently it is similar to rapid and canalised rivers, while different from the canals;- The following is  decisive for determination of the navigable riverbed depth in two-way navigation:  the central navigation in direction and full speed of the vessel or the convoy. The determined depth accounts for the whole width of the navigable riverbed;- The longitudinal trim of a vessel according to experience is adopted with s: t = 0,1 [m];- The values of the speed sink Sz for IV to VII class of the navigable way on the canals and rivers are read off or estimated from the Kuhn ` s experimental diagrams [4]. As there are no diagrams for all the classes, the next closest diagrams were used. With the rivers of I, II. and III. class the expression according to Wiegleb was applied  [6]; - The absolute reserve for I. to IV. class is taken as:  = 0,3 [m], for V. class  = 0,4 [m], for VI. a and b class  = 0,5 [m], and for VI. c and VII. class  = 0,6 [m]; - The arbitrary size  = 0,3 [m] is taken as a reserve due to the imprecision of a measurement.

The reserve due to the inexactness of the cut of the navigable way transversal profile in the subject area is taken as s  = 0,3 [m];- The recommended navigable way depth for the full draught is to be secured at V65% AGN [5];- In this classification, it is recommended for shorter rapid rivers that reach the depth of the navigable bed for the full draught only at high water levels with the NVP (that matches the water level of 95% durability) to lower the navigable bed depth up to 60% of depth calculated for the full draught according to;- It is assumed that canalised rivers, built as artificial watercourses intended for navigation, should guarantee a safe navigation with a full draught with NVP, which  corresponds to the water level of 95% of durability;- Here is adopted that canals as the artificial facilities serving to navigation should be built to guarantee safe navigation at the full draught "at each moment "; that means, with the NPV that suits the constant water level in the canal.

|  |  | IV | Va | Vb | Via | VIb | VIc | VII |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Speed sink (m) | 0,4 | 0,4 | 0,4 | 0,6 | 0,5 | 0,6 | 0,6 |
|  | Longitudinal trim (m) | 0,1 | 0,1 | 0,1 | 0,1 | 0,1 | 0,1 | 0,1 |
|  | Inexactness (m) | 0,3 | 0,3 | 0,3 | 0,3 | 0,3 | 0,3 | 0,3 |
|  | Absolute reserve (m) | 0,3 | 0,4 | 0,4 | 0,5 | 0,6 | 0,6 | 0,7 |
|  | Draught (m) | 2,5 | 2,8 | 2,8 | 2,8 | 2,8 | 2,8 | 4,5 |
|  | Total (m) | 3,6 | 4 | 4 | 4,3 | 4,3 | 4,4 | 6,2 |

Fig. 5 Diagram of the final parameter recommendations for the navigable riverbed depths, for the IV to VII navigable waterway classes.

##### References

[1]	UN/ECE: United Nations / Economic Commission for Europe: CLASSIFICATION OF EUROPEAN INLAND WATERWAYS, Geneva 1960. [10]

[2]	UN/ECE: United Nations, Economic and Social Council, Economic Commission for Europe,Inland  Transport Committee: CLASSIFICATION OF EUROPEAN INLAND WATERWAYS, Resolution No. 30, TRANS/SC.3/131, str. 183, Geneva November 1992. [9]

[3]	Der Bundesminister für Verkehr: RICHTLINIEN FÜR REGELABMESSUNGEN DES NORD - WESTDEUTSCHEN KANALNETZES, Der Bundesminister für Verkehr, Abteilung Binnenschiffahrt und WasserstraßenWasser und Schiffahrtdirektion, Hanover, 1990.

[4]	Kuhn R.: BEMESSUNGSGRUNDLAGEN FÜR DIE FAHRWASSERTIEFEN DES EUROPAKANAL RHEIN - MAIN - DONAU, Schiff und Hafen, 25 Jhg.H1, Seehafen Verlag Hamburg 1973.

[5]	AGN: EUROPEAN AGREEMENT ON MAIN INLAND WATERWAYS OF INTERNATIONAL IMPORTANCE (AGN), United Nations, Economic Commission for Europe, Inland Transport Committee, Geneva, 19 January1996.

[6]	Wiegleb K.: WASSERTECHNIK, Band 4, Verlag für Bauwesen GmbH, Berlin, 1997.

[7]	PIANC: FACTORS INVOLVED IN STANDARDISING THE DIMENSIONS OF CLASS Vb INLAND WATERWAYS (CANALS), International Navigation Association, Report of Working Group nº20 of the Permanent Technical Committee I, PIANC, Supplement to Bulletin nº101, 1999.

[8]	Graewe H.: BEITRAG ZUR FRAGE DER BEMESSUNG VON FAHRWASSER-VERBREITERUNGEN IN KANAL - UND FLUSSKRÜMMUNGEN, Die Bautechnick, H.1, Berlin 1971.

[9]	Commission du Danube: RECOMMANDATIONS RELATIVES A L’ETABLISSEMENT DES GABARITS DU CHENAL, DES OUVRAGES HYDROTECHNIQUES ET AUTRES SUR LE DANUBE, Budapest 1975.

[10]	Partenscky H. - W.: BINNENVERKEHRSWASSERBAU: Schleusenanlagen, Springer - Verlag Berlin Heidelberg New York Tokyo, 1986.