Prof. Josip Marušić, Ph.D.C.E.

Prof. Marko Pršić,Ph.D.C.E.

Duška Kunštek, MS,C.E.

THE PREPARATIONS FOR DANUBE – SAVA MULTI – PURPOSE CANAL

SUMMARY

The paper deals with the current state of preparations for the canal construction: exploratory works, development and planning documentation projects and preliminary works. It also focuses on construction dynamics adjusted to state irrigation programme.

Key words:

Danube – Sava multi – purpose canal, inland navigation, development and planning documentation projects, construction

1.	Chronology of development and planning project documentation of DSMC

Development - planning documentation and traffic development strategy of Croatia from 1999 defined the development of Croatian inland waterways along with Danube – Sava multi – purpose canal - DSMC project was. The DSMC project was completed late in 1998 and early in 1999 the State administration for environmental protection reached an AGREEMENT stating that DSMC was environmetally friendly project. Unfortunately, from 2001 to 2004 the activities on completion of study and project documentation of DSMC were interrupted by the decision of  the then Ministry for public works, rebuilding and construction. Since 2005 the works on completion and upgrading of development and planning documentation, studies and  projects for DSMC were resumed to the level necessary to obtain location and preliminary building permission – with completion term in 2007. g.

According to accepted and signed AGN agreement, next to the navigable sections of the rivers  Danube, Sava and Drava the DSMC project fell also into the system of European navigable ways by the parameters of V.b class of international inland waterways. Bearing on mind economic and environmental benefits of inland waterway traffic, the significance of DSMC lies in connecting Croatia with the European system of inland waterways. It also acts as an integral part of successful economic development and incorporation with the states of Danubian and Adriatic region.

Study and project documentation for DSMC from 1995 to 2006

In 1988 started the works on "Development Planning of Danube – Sava Multipurpose Canal Corridor" as a result of many initiatives for documentation basis, and by the decision reached by the local municipality. The decision was made according to the then legal Law on development planning and space arrangement by the municipalities of Vinkovci, Vukovar, Županja and Slavonski – Brod. The development plan based on Preliminary canal project: "Danube – Sava Multi-purpose canal, a solution variant ", books I - III", Hidrozavod DTD, Novi Sad, elaborated in 1985, and revised by the Institute of Civil Engineering in Zagreb. It was completed in 1997, but never adopted, since according to the then "Law on development planning " (NN number 30/95) there was no obligation of development plans for infrastructure corridors. Later, such regulations were introduced, but the adoption of  Development plan was not initiated. During the creation of the first phase of corridor’ s Development plan it was noticed that the Preliminary design from 1985 did not represent suitable basis  for further planning and design, with regard to  insufficiently detailed project and numerous modifications coming up in the meantime. Late in 1995, parallel with formation of Development plan started the completion of "Annex to preliminary design of the Danube – Sava multi – purpose canal ". The project was completed in 1998. "Preliminary design of the port of Vukovar " on the D-S canal was completed in 2000.  Until the year 2000 twenty two institutions and companies with 156 renowned professionals and researchers of all needed fields took part in terrain works and creation of study and project documentation within the Annex of preliminary design of DSMC. Within the Annex, the Environmental Impact Study of D-S canal was developed.  The environmental protection committee reached the DECISION on 16 March 1999 to determine the DSMC project as environmentally friendly, while including the environment protection monitoring in the programme implementation. From 2000 to 2005 the  monitoring was conducted with results confirming the impact of DSMC on forest ecosystems, whereby pointing at its significance for control and maintenance of underground water level on gravitation area of agricultural soil.

Location permit for canal construction D-S was demanded during 1999. The then Ministry of development planning did not incite the local permit procedure as the planned operation and documentation were not adjusted to legal framework and existing development and planning documentation. In this way all the activities for obtaining the D – S local permit were interrupted. Moreover, the conditions needed for canal construction were not mature. After the interruption in 2001 the activities and completion of project documentation were resumed only in 2005.

Activities and operations on completion and upgrading of study and project documentation of DSMC in 2006 and 2007

After several expert debates (2004 and 2005) conducted by heads and chief executives of activities in working out of study and project documentation supplied by explanations of authorized ministries (MPŠVG, MZOPUG, MMTPR) the programme proposal was accepted in collaboration with the Agency for navigable inland waterways in May of 2006:

The completion of development and planning documentation for the project study level (preliminary design upgrading, environmental impact estimation, completion of expert documentation for location permit and obtaining of local permit), geodesic works, upgrading of  geotechnical investigation works, preparation of  geotechnical investigation works for the main design, upgrading of preliminary design, and completion of legal procedure (obtaining of preliminary permit) for the construction of DSMC.

After completed tender on 29 June 2006 the Agreement on execution of mentioned operations was signed between the Agency for navigable inland waterways – PERFORMER and the Institute of Civil Engineering of Croatia, in collaboration with the Faculty of Civil Engineering University of Zagreb, Water Management –project office d.d., Zagreb, Institute for Geodesic Operations d.d. Osijek, Institute for Development Planning Osijek and Elektroprojekt d.d. Zagreb. In order to complete the project and other documentation, a solution on the use of earth material needed for the cut of DSMC and further construction of V.c motorway CORRIDOR should be submitted, along with the project of irrigation of agricultural soil.

The deadline for operations and upgrading of planning, study, project and other documentation for DSMC is late June of 2007 – including location permit procurement and by the end of September the procurement of  preliminary permit.

Activities in elaborating the upgraded technical documentation of DSMC consist of the following steps:

- Development planning documentation

- Upgrading of preliminary design (from 1998)

- Environmental impact estimation of DSMC (Upgrading of Environmental impact study from 1999.)

- Completion of feasibility study –  in accordance with development documentation (alterations and annexes)

- Obtaining of location permit

- Upgrading of preliminary design– with facilities on DSMC

- Preliminary permit for DSMC

- Upgrading of geotechnical study

- Geodesic operations for DSMC.

2.	Feasibility of Danube – Sava multi – purpose canal

Multifunctional significance of a future canal is contained in the following: irrigation, navigation and drainage, and in a number of subsidiary activities like: enrichment of small waters, technological water and positive environmental  effects.

Fig. 1	Areas planned for irrigation, according to canal construction phases

The strategic goal of irrigation of 35.750 ha of agricultural soil would lead not only to the increase of the already highly productive traditional farming, but also to the alteration of market based vegetation plants’ sowing structure. (Fig. 1).

The canal navigation in the framework of Croatian strategic traffic policy should be regarded only from the aspect of constructing the 570 km long Podunavlje-Jadran traffic corridor (Fig. 2). The river – railway connection is scheduled to consist of: 61,4 km of Danube – Sava canal (from Vukovar to Šamac), 306 km of canalized river of Sava from Šamac to Sisak with  2 water reaches (Županja and Jasenovac) and 200 km of  Sisak-Zagreb-Rijeka double track railway (currently 230+50km, mostly single track). The aim of drainage of the canal catchment is to arrange further  the surface drainage on 173.000 ha and to ensure conditions of extending underground drainage on 62.000 ha of agricultural soil. The other aim is the elimination of temporary long lasting and uncontrolled floods of Spačvansko-studvanski basin and the regulation of its discharge water  according to the needs of forest vegetation. The enrichment of small waters  is connected with irrigation and environment of canal based settlements. The canal ensures also the use of technologic water

Fig. 2	Podunavlje – Jadran traffic corridor 2

3	Basic construction elements

The future D-S canal would involve the construction of the following:

- 61,4 km  of DSMC,

- 8,6 km of DC

- Two ship locks,

- Six weirs,

- Three pumping stations,

- One siphon,

- 20 road and

- 3 footbridges and cycling bridges,

- 4 railway bridges,

- 770 m of pedestrian and bike approaches,

- 30.036 m of road approaches,

- 12.028 m railway approaches and

- A series of minor facilities on the canal and onshore

The operations will encompass:

Digging and disposal of:

- 54 mil. m3 of earth material

Embedding of:

- 2.6 mil. m3 of stone material,

- 260.000 m3 of concrete

- 20.000 t of steel.

Within the broader canal zone (±500[m] from the axis) there are 62 existing and 25 scheduled electric and phone cables. 38 of existing ones and 12 scheduled ones cross the Canal. In addition, in the broader zone of the Canal (±500[m] from the axis) there  are 21 power transformers.

To connect the future D-S canal and accompanying facilities to the existing system of electric supply the following is needed:

- To install 5 future power transformers into the system

There are 2 existing gas pipelines and 2 next are scheduled, along with two oil pipelines within the broader canal's zone.

Fig. 3	Danube-Sava canal route with facilities 3

Within the broader canal zone there are 10 existing and 3 planned water supply systems. 9 of the existing water supply systems and 3 that are scheduled would cross the canal. Further, 7 main collectors are planned, 4 of them crossing the canal.

4	Construction phases

DSMC construction scenarios result from development strategy and programme, and particularly irrigation of agricultural soil, construction of Kneževo – Velika Kopanica road corridor Vc, snd improvement of forests’ water regime to increase the crops and meet environmental needs.

The scenarios simulate possible final stages of canal construction and act as operable units:

- SCENARIO I	First 15 km of Canal from Sava to Konjsko canal for irrigation

- SCENARIO II	The whole DSMC constructed at the same time from Sava to Danube

- SCENARIO III	The whole DSMC constructed at the same time from Sava to Danube  with the port of  Vukovar on the Canal

The time period of 61,5 km Canal would stretch possibly  according to the SCENARIO II, throughout 4 phases, not necessarily involving the mentioned dynamics. Each of proposed development phases represent one hydro-engineering unit that could independently function until the extension in the next phase. As far as for the planned purposes, they are unlimited regarding the time. The development within each single phase could run throughout several stages depending on  area development and scheduled utilization: irrigation, drainage and navigation. The traffic function would be partly introduced in the Phase II.  and entirely   in the Phase IV. Irrigation will be to a large extent realized already in the Phase I (Fig. 4).

The Investor defined the following phases development of the future D-S Canal on the basis of conducted analyses (technical, economic and management).

- Phase I is concerned with ensuring conditions for the irrigation of agricultural areas of the Biđ-Bosut field (BBP) and the forest area of Spačva.  It would also encompass the canal construction  along the planned route from the river of Sava to the link with the Biđ watercourse (the length of 15 km), to ensure conditions for water supply from the  river of Sava into major recipients on the greater Biđ and  Bosut areas. The riverbed cut would be  conducted in reduced dimensions. At the link with the Sava river on the diversion channel  of Sava, the weir and pumping station would be built, over which the needed water quantities would be conducted into the Canal and farther into the system of existing BBP canals not only in this phase(but also later). At that period only the weir and pumping station  of the Sava junction will be built. On the D-S’s canal profiles with the existing traffic network the temporary culverts would be constructed.

- Phase II is the largest and most important, as it contributes to the regulation of water regime of large and small waters on the BBP area and ensures conditions for the navigability to Vinkovci from the direction of Danube. These operations would ensure drainage of massive waters from BBP into the Danube besides the existing drainage into the Sava. It will all make possible to manage large waters on the BBP area, water supply into the BBP system and from the Danube in order to enrich small waters to enable irrigation of Biđ-Bosut field and Spačva-Studva forest complex. This phase would cover approximately 25 km of future D-S canal with riverbed’s full profile. Most of water facilities will be built, some of them outside the borders of mentioned 25 km of the Canal. The crossings of traffic and infrastructure links according to their location and dynamics are considered on the section in question considering special characteristics of DSMC from Development plan.

- Phase III includes the extension of the navigable way from Vinkovci to Cerna. The DS canal would be constructed along the existing watercourses: Bosut, Bazjaš and Biđ in the length of cca 22 km, in the full riverbed profile. The landing at Cerna and weir at Vezovac will be erected. The crossings of traffic and infrastructure links according to their location and dynamics are considered on the section in question considering special characteristics of DSMC

- Phase IV leads to the full operability of Danube - Sava navigable way. It overlaps in developmental aspects with the I. phase section. The cca 15 km Canal's full profile would be constructed, e.g. it would contribute to a large riverbed profile extension from the I. phase. The Sava junction lock would be constructed. The crossings of traffic and infrastructure links according to their location and dynamics are considered on the section in question considering special characteristics of DSMC. The construction of Zagreb-Lipovac motorway over the Canal is considered as a demanding operation.

Fig. 4	The Danube – Sava canal route with facilities 4

PHASE II CANAL CONSTRUCTION FROM DANUBE TO BOSUT – FULL CANAL PROFILE cca 25 km

PHASE III – FROM VINKOVCI TO BIĐ – FULL CANAL PROFILE ACCORDING TO EXISTING BEDS cca 22km

Phase IV  FROM BIĐ TO SAVA – FULL CANAL PROFILE cca 15km (SECTION OF THE Ist PHASE DEVELOPMENT)

The operations of the I. and II. Canal’s development phases overlap. Their construction is estimated to take between 8 – 10 years. The operations of the III. and IV. canal’s development phases can overlap as well, but at any time after or parallel with the  II. Phase. It is difficult to estimate the start of this phase. However, the construction could take  4 to 5 years.

The Table I provides the illustration of Canal’s development stages by listing future facilities, whereas the illustrations (Fig. 5 to 7), in the appendix show the operations according to development stages, along with the basic aims containing the phases of proposed solutions.

Table I 	Illustration of development phases of DSMC through the list and position of designed facilities 2

Fig. 5	I.phase development system of DSMC 2

PHASE I DSMC DEVELOPMENT SYSTEM IN THE FUNCTION OF INTRODUCING ADOPTED IRRIGATION PLANS ON THE BBP AREA

BASIC AIMS ARE:

- ENSURING CONDITIONS FOR IRRIGATION OF 4.000 – 8.000 ha (Ist development stage of irrigation from DS canal) and –

- Creation of acceptable environmental conditions in the watercourses of small waters

Fig. 6	Objectives of II. development phase of DSMC system 2

PHASE II DSMC DEVELOPMENT SYSTEM IN THE FUNCTION OF SMALL AND LARGE WATER REGIME REGULATION AND ARRANGEMENT OF NAVIGABLE WAY TO VINKOVCI

BASIC OBJECTIVES ARE:

- LENDING OF MATERIAL FOR FACILITIES CONSTRUCTION ON THE Vc COORIDOR

- MANAGING OF WATERS ON THE BBP  - LARGE WATER: DRAINAGE INTO DANUBE, SMALL WATER: INTAKE (SUPPLY) OF ADDITIONAL WATER QUANTITIES FOR IRRIGATION AND ECOLOGY,

- NAVIGABILITY TO VINKOVCI AND

- ENSURING OF CONDITIONS FOR DEVELOPMENT OF MANAGEMENT ZONE AT BRŠADIN AND THE CONSTRUCTION OF NEW PORT ON THE CANAL

THE PERFORMED WORKS OF PHASES I AND II ENSURE COMPLETELY THE PLANNED CONDITIONS OF THE REGULATORY (WATER REGIME) ROLE OF THE FUTURE DS CANAL

Fig. 7	Objectives of III. and IV. development phases of DSMC system 2

PHASES III AND IV DSMC DEVELOPMENT SYSTEM IN THE FUNCTION OF THE FINAL ARRANGEMENT OF “DANUBE – SAVA” NAVIGABLE WAY

5	Construction expenses

| INVESTMENTS INTO THE PORT AND CANAL | SCENARIOS |
| --- | --- |
|  | I | II | III |
| Construction expenses of canal's infrastru. On the debit of RC | 46 mil. EUR | 827 mil. EUR | 827 mil. EUR |
| Construction expenses of canal's infrastru. on the debit of RC | 0 | 0 | 300 mil. EUR |
| TOTAL RC | 46 mil. EUR | 827 mil. EUR | 1.127 milijardi EUR |
| Construction expenses of infrastr. on concessionaire's debit | 0 | 0 | 450mil. EUR |
| INVESTMENT EFFECT ACCORD. TO SCENARIOS (with 5% of credit interests) |  |  |  |
| Cash property refund (years) | 4 | 26 | 28 |
| IRR after 50 years | 25,75% | 5,48% | 5,79% |

Tab II	 Investment costs into DSMC and the port of Vukovar

Table III gives the canal's costs estimate according to phases

|  | TOTAL CONSTRUCTION EXPENSES BY PHASES (INCLUDING ELECTR..MACHINERY AND HYDROENG. EQUIPMENT) | CUMMULATIVE |
| --- | --- | --- |
|  | [€] | [€] |
| PHASE I | 45.316.129 | 45.316.129 |
| PHASE II | 399.345.990 | 444.662.118 |
| PHASE III | 210.671.556 | 655.333.674 |
| PHASES V IV | 171.405.102 | 826.738.775 |

Table III	Illustration of construction expenses of DSMC through development stages 2

Investment comparison for 1m' of Canal:

- Construction expenses for Danube –Sava  canal (Vb)		9,6 mil.EUR/km

- Construction expenses of Main-Danube canal (Vb)	10,24    mil.EUR/km

- Construction expenses  of Cernavoda-Constanta canal (VII)	19,7      mil.EUR/km

6	What has to be done in future

- Agreement between RC & B and H & S and CG on possible common development of  Podunavlje – Jadran traffic corridor within the Sava initiative

- To reach the decision of the Croatian government on the Danube – Sava canal construction+  construction scenario + model and financing resources

- Upgrading of development, planning and conceptual documentation for DSMC

- Defining of proprietary legal relations on the building area. Adoption of environmental impact study for the port of Vukovar

- Procurement  of location permit

- Area demining for the port of Vukovar

- Remaining investigation work

- Proprietary conditions on the building area

- Main design

- Procurement of a building permit

- Tender procedure

Literatura:

- ''Plan natapanja uz višenamjenski kanal Dunav – Sava'', Hidroing d.o.o., Osijek, 1997.

- ''Upgrading prostornoplanske i idejne documentation višenamjenskog kanala Dunav – Sava, Knjiga D1: Preliminary design kanala i vodnih građevina'', Građevinski fakultet Sveučilišta u Zagrebu, Zagreb, ožujak 2007.

- “Dopuna preliminary designvišenamjenskog kanala Danube - Sava, Knjiga A, Sažetak”, Vodoprivredno - projektni biro, Zagreb, prosinac 2001.g.

- “Studija etapnog razvoja VKDS”, Vodoprivredno - projektni biro, Zagreb, srpanj 2006.g.

- Marušić, J. (1999.): Značenje ''Višenamjenskog kanala Dunav-Sava» za gospodarsko povezivanje Podunavlja s Jadranom'', HAZU, Zagreb, Anali, Osijek, str. 57-88.

- ”Strategija prometnog razvitka Hrvatske u 21. stoljeću (2001.)”, Ministarstvo pomorstva, prometa i veza, Zagreb.

- Marušić, J. (2002.): ”Economic Importance and the Environment of the Multipurpose Danube-Sava Canal”, Transport and Environment, Symposium, Modern Traffic, Opatija, Croatia, 2002, pp 66-71.

- Marušić, J., Kolovrat, I. (2004.): ”Značenje i problemi ostvarenja projekta Višenamjenskog kanala Dunav-Sava”, Sabor hrvatskih graditelja 2004., Cavtat.

- Martinčić, J., Marušić, J., Legac, I. (2004.): ”Gospodarsko povezivanje Podunavlja s Jadranom - dosadašnja istraživanja kao okosnica saznanja o prometnom pravcu «Baltik – Srednja Europa – Jadran»”, Koridor V.c kao poveznica na prometnom pravcu «Baltik – Srednja Europa – Jadran», Osijek, str. 47-57.

- Marušić, J., Pršić, M. (2005.): ”Značenje unutarnjih plovnih putova za prometno povezivanje Hrvatske i Podunavskih zemalja” «Prometna povezanost Hrvatske s europskim zemljama u funkciji razvoja sjeverozapadne Hrvatske, HAZU, Varaždin, str. 147-162.

- ”Prijedlog aktivnosti i poslova za dovršenje studijske i projektne documentation VKDS u 2006. g.”, Vodoprivredno-projektni biro d.d. Zagreb, Građevinski fakultet Sveučilišta u Zagrebu, Hrvatske vode Zagreb, Uprava vodnog gospodarstva – MPŠVG: Zagreb, svibanj 2005. i ožujak 2006.

- Marušić, J. (2006.): ”Višenamjenski kanal Dunav – Sava u funkciji KORIDORA 5c.” Znanstveni simpozij «Saobraćajni sistem KORIDORA 5c – nove mogućnosti razvoja, Sarajevo, str. 251-256.

- Marušić, J., Kolovrat, I. (2006.): ”Višenamjenski kanal Dunav-Sava, osnovni pokazatelji o studijskoj i projektnoj documentation od 1991. do 2005. g.,” 3. Međunarodni znanstveni simpozij KORIDOR 5c – kao euroregionalna poveznica na prometnom pravcu Baltik – Srednja Europa – Jadran, Osijek – Vukovar.

- ”Documentation za nadmetanje – upgrading i dovršenje prostorno-planske, studijske i projektne documentation VKDS”, Agencija za plovne putove unutarnjih voda, Zagreb – Vukovar, 2006.

- ”Izvještaji o novelaciji i dovršenju prostorne, studijske i projektne documentation VKDS”, Građevinski fakultet Sveučilišta u Zagrebu, Vodoprivredno projektni biro d.d. Zagreb, Agencija za plovne putove unutarnjih voda i IGH, Zagreb, 2006. i 2007.

# Footnotes

Faculty of Civil Engineering University of Zagreb

Kačićeva 26, 10000 Zagreb

Tel. (1) 4639-612 Fax (1) 4639 260, E – mail: marusicj@grad.hr

Faculty of Civil Engineering University of Zagreb

Kačićeva 26, 10000 Zagreb

Tel. (1) 4639-358 Fax (1) 4639 260, E – mail: mprsic@grad.hr

Faculty of Civil Engineering University of Zagreb

Kačićeva 26, 10000 Zagreb

Tel. (1) 4639-101 Fax (1) 4639 260, E – mail: kduska@grad.hr

# Text boxes

PHASE I – WATER SUPPLY FROM SAVA INTO MAJOR RECEPIENTS OF THE BBP AREA (SAVA – BIĐ)- REDUCED CANAL PROFILE (cca 15km)