A CONTRIBUTION TO THE DETERMINATION OF GROUP TYPE DISTRIBUTION OF AROMATIC IN PETROLEUM MIDDLE DISTILLATES BY NPHPLC

Tatjana Tomić1, Nikola Šegudović1, Nada Uzorinac1, Liviana Škrobonja2

1 INA-INDUSTRIJA NAFTE d.d.,

Corporate Processes Research and Development Sector Central Research Laboratory, Zagreb

2INA-INDUSTRIJA NAFTE d.d., Rijeka Oil Refinery, Rijeka

Key words: aromatic hydrocarbons, petroleum, NPHPLC

The knowledge of the group-type distribution of aromatic and polycyclic aromatic compounds in petroleum middle distillates is a very important parameter for final properties from the aspects of application and environmental requirements. The determination of group-type distribution by NP HPLC is regulated by the standard methods of EN 12916 or ASTM-6591[1]. The determination of aromatics in middle distillates is generally carried out by means of normal phase high-performance liquid chromatography (NP-HPLC) with refractive index detection (RID), NH2 column, n-heptane as the eluent and column backflush. The content of particular species ranges from trace (tri+aromatics, TA) to percentage level of mono-aromatics and as a method is not absolute, the accuracy being calibration-dependent. Use of RI detector leaves no doubt in regard to mono-aromatics and di-aromatics determination, but the limit of quantification for tri+aromatics is 0.1%, due to a very low refractive index difference at the required concentration. As environmental regulations force to reduce the amount of polyciclic aromatics, especially tri+aromatics, there is a need for a more sensitive detection. The UV detector is particulary suitable for the determination of very low contents of polycyclic aromatics [2].

The EN 12916 method requires a mass % of standard solutions and results are delivered also in mass %. Some uncertainty is involved in preparation of standard solution due to a very low amount of tri+aromatics. To overcome this possibility in this work a different approach has been proposed. Only the highest concentration of aromatic standard (solution A from EN 12916 method) is prepared by weighing, while all other solutions (B,C,D) just by diluting the A solution.

Picture 1. Kalibration curve for di-aromatics, DA with RI

Picture 2. Kalibration curve for di-aromatics, DA with UV detection

Picture 3. Kalibration curve for tri+aromatics,TA with RI

Picture 4. Kalibration curve for tri+aromatics,TA with UV detection

A second contribution to the calibration curve accuracy is based on a different fitting procedure in the obtained calibration curves (ignore zero, force zero and include zero)

| Detection mode | Equitation of calibration curves | Correlation coefficient | Fitting |
| --- | --- | --- | --- |
| RI detection |
| MA | y=4,802x105+5,849x103 | 0,9999 | Linear, include |
| DA | y=8,270x105+2,716x103 | 0,9999 | Linear, include |
| TA | y=1,053x106+2,406x103 | 0,9997 | Linear, include |
| UV detection |
| MA | y=1,586x106-1,370x103 | 0,9998 | Linear, include |
| DA | y=1,439x107+3,548x104 | 0,9995 | Linear, include |
| TA | y=1,935x108+6,840x104 | 0,9992 | Linear, include |

Table 1. Calibration curves equitations

The difference in the determined content of polyciclic aromatics by UV-DAD and by RI detection is not negligible and depends on the type of aromatic and source of calibration curves. The differences are more pronounced in case of mono-aromatics.

In this work numerous middle distillate samples were analyzed and contents of aromatic species were determined. The applied method precision was checked by determination of repeatability, by standard and relative standard deviations (SD, RSD). The limits of detection and quantification were also determined.

| Sample | MA (m/m)% | DA (m/m)% | TA (m/m)% | polyA (m/m)% | total A (m/m)% |
| --- | --- | --- | --- | --- | --- |
| Kerosene | 17,3 | 1,5 | - | 1,5 | 18,8 |
| Light gas oil | 15,4 | 6,4 | 0,9 | 7,3 | 19,7 |
| Eurodiesel fuel | 20,8 | 1,4 | 0,1 | 1,5 | 22,3 |
| Diesel fuel | 17,7 | 6,4 | 1,0 | 7,4 | 25,1 |

Table 2. Aromatic group type composition (wt%) of different middle distilates (RI detection)

| Sample | MA (m/m)% | DA (m/m)% | TA (m/m)% | poli-A (m/m)% | total A (m/m)% |
| --- | --- | --- | --- | --- | --- |
| Kerosene | 14,8226 | 2,1585 | 0,0001 | 2,1586 | 16,9812 |
| Light gas oil | 10,7897 | 8,0458 | 0,7918 | 8,8376 | 19,6273 |
| Eurodiesel fuel | 11,2272 | 2,3560 | 0,0988 | 2,4548 | 13,6820 |
| Diesel fuel | 10,4617 | 7,1144 | 0,6728 | 7,7872 | 18,2489 |

Table 3. Aromatic group type composition (wt%) of different middle distilates (UV detection)

Lit:

[1] Petroleum products- Determination of aromatic hydrocarbon types in middle distillates- High performance liquid chromatography refractive index method, European Standard EN 12916-00

[2] M. Kaminski, E.Gilgenast, A. Przyjazny, G. Romanik, J. Chromatogr. A, 1122(2006)153