Putting Carbon Dioxide Back into the Subsurface - Possibilities in Croatia

Bruno SAFTIĆ(1), Iva KOLENKOVIĆ(2) and Domagoj VULIN(3)

University of Zagreb – Faculty of Mining, Geology and Petroleum Engineering, HR-10000 Zagreb, Pierottijeva 6

- Phone: 385 1 5535772, e-mail: bruno.saftic@rgn.hr

- Phone: 385 1 5535761, e-mail: iva.kolenkovic@rgn.hr

- Phone: 385 1 5535846, e-mail: domagoj.vulin@rgn.hr

Abstract: Capture and geological storage of CO2 represents an option to avoid emissions of this greenhouse gas into the atmosphere, by capturing CO2 from major stationary sources, transporting it by pipelines or ships and injecting it into deep underground reservoirs. Deployment of these systems could help Croatia to stay within the limitations set by the Kyoto Protocol. There are reservoir formations with favourable conditions in the southern Pannonian basin as well as in the Adriatic off-shore that could be prepared for geological storage. Depleted oil and gas reservoirs might be the most promising in the beginning, particularly in the initiated EOR operations, but much larger potential can be assigned to the regionally extending deep saline aquifers.

Keywords: carbon capture and storage (CCS), geological storage capacity, depleted hydrocarbon fields, deep saline aquifers, Pannonian basin, Adriatic off-shore, Croatia.

- INTRODUCTION

To prevent the increase of global warming and its negative impacts, significant reductions of anthropogenic greenhouse gas emissions have to be obtained. In order to achieve this goal, different reduction measures have to be applied, including fuel switching, increasing of energy efficiency and energy conservation, using of renewable energy sources and capture and storage of CO2 (PACALA & SOCOLOW, 2004).

There are three different types of CO2 storage: storage in deep geological reservoirs, storage through surface mineral carbonation and storage in oceans (IPCC, 2005). Mineral carbonation is expensive, slow and it has a significant impact to the environment. Ocean storage is disadvantageous option because it affects the acidity of the ocean, meaning that it could endanger ocean organisms and have severe impact on ecosystem (IPCC, 2005). Carbon capture and storage (CCS) on the other hand, represents a technology that is in principle available and technologically feasible due to the experience from oil and gas exploration and production, deep waste disposal and groundwater protection. Also, capacities for geological storage of CO2 are quite large, although not evenly distributed. Geological storage can provide long-term solution, because of long retention times that can be even millions of years. However, there are still a lot of issues to be solved before the immediate full-scale implementation of CCS, issues mostly being related to a general lack of knowledge about the location and capacity of potential geological storage sites (CSLF, 2007; IPCC, 2005).

Geological storage of CO2 can be performed in various geological settings in sedimentary basins. Possible storage options include geological trapping in depleted oil and gas reservoirs, solubility trapping in producing oil reservoirs, adsorption trapping in unmineable coal seams and hydrodynamic trapping in deep saline aquifers (BACHU, 2000; 2003). In addition to storage in sedimentary formations, possibilities for storage in caverns (cavern trapping in salt structures and by mineral immobilization), basalts and organic-rich shales are being considered. Options for storing CO2 in various geological media are shown in Fig. 1-1.

Fig.1-1. Different possibilities for storage of CO2 in geological media (from Bachu, 2003)

Geological storage of CO2 is achieved through a combination of physical and chemical trapping mechanisms that are shown in Fig.1-2 (IPCC, 2005). After the injection, CO2 migrates through the reservoir at velocities dependent on the reservoir properties and gradually becomes trapped by different trapping mechanisms. Physical trapping of CO2 occurs when CO2 is stored in geological formation - within stratigraphic and structural traps, or rarely in man-made caverns. Structural traps represent sealed geological structures formed by folding or faulting, capable of retaining fluids due to impermeable cover of cap rocks. Stratigraphic traps are sealed systems of rocks with reservoir properties where the main elements of closing are pinching-out of porous and permeable rocks, lateral gradation of sand towards shale, or erosion and transgressive cover of younger impermeable rocks. Both, structural and stratigraphic traps are suitable for CO2 storage, although care must be taken not to exceed the maximal overpressure to avoid fracturing the cap rock or re-activating faults. Hydrodynamic trapping is a type of physical trapping that occurs when CO2 slowly flows through the saline formation, firstly upwards, due to buoyancy forces. When it reaches the top of the formation, it continues to migrate as a separate phase until it is trapped in the interstices of the grains in the rock as a result of the surface tension of the CO2 phase (residual trapping) or in local structural or stratigraphic traps formed below the cap rock (CSLF, 2007; IPCC,2005). After a considerable time, significant amount of CO2 dissolves in the formation water and chemical trapping takes place. When the CO2 is dissolved, it no longer represents a separate phase, so that the buoyant forces that drive it upwards disappear. The solution may react with the rock to form ionic species (ionic trapping). Also, geochemical reactions between solution and rock may result in creation of stable carbonate minerals (mineral trapping), a long-lasting process that lead to the most permanent form of geological storage. If the CO2 adsorbs onto surface of minerals, adsorption trapping happens.

Fig.1-2. Trapping mechanisms which enable geological storage of CO2 (IPCC, 2005)

The efficiency of the geological storage of CO2 depends upon different factors, including buoyancy of CO2, formation water density, lithological heterogeneity and mineralogical composition of a storage formation. The trapping security has to be evaluated within a risk analysis that has to be carried out for each storage site.

2. POSSIBILITIES FOR GEOLOGICAL STORAGE IN CROATIA

Republic of Croatia became a party to the United Nations Framework Convention on Climate Change (UNFCCC) in 1996. Croatia has also signed and later ratified the Kyoto Protocol taking the obligation to reduce the greenhouse gas emission by 5% in the 2008-2012 period.

Major part of CO2 emissions in Croatia is from thermal power plants, municipal/district heating plants, and oil industry activities (2800 kt CO2/yr) as well as other industrial processes (EKONERG, 2005). The largest concentrated stationary sources are the 7 coal, gas and/or oil power plants. Mainly due to the increased economic activity, their emissions were constantly rising in 1990-2003 period. The locations of these facilities are shown in Fig. 2-3. Total power plant emissions in 2003 were 5478 kt CO2/yr which is 24% of the total CO2 emissions in Croatia. There is also one large point source in the national oil industry. This is the natural gas processing plant “Molve”, located in the western part of the Drava river valley, close to Hungarian border (Fig. 2-3). In 2004 a total of 684 kt of CO2 were separated there from the natural gas streams and released in the atmosphere. Presently, this plant is the primary candidate for the carbon dioxide capture and subsequent use in EOR operations.

The fact that the emissions from point sources in Croatia amount to 26% of total CO2 emissions, actually allows significant reductions to be made by carbon capture and storage systems.

2.2 Geologic composition in the subsurface

Subsurface geological relations are the first critical factor to estimate the geological storage potential. These relations have been defined in the course of petroleum-geological exploration mainly in the last 60 years. There are three parts of the Croatian territory that have some common characteristics regarding the generation and accumulation of oil and gas. These large units are called hydrocarbon-bearing provinces – Pannonian basin, Dinarides and Adriatic offshore. Only the first and the third province can offer locations with favourable conditions for geological storage of carbon dioxide, the Dinarides can largely be ruled out due to several reasons. Firstly, this mountain region is in Croatia largely composed of Mesozoic carbonates that are karstified to depths exceeding 1000 m. Karst hydrogeological system and its groundwater resources effectively prevent any type of geological storage in that region. The other reason is the high neotectonic (and seismic) activity which would put installations and subsurface storage objects at risk. This means that looking for the favourable natural conditions should be directed both to the southern part of the Pannonian basin and to the Adriatic off-shore.

Pannonian basin  The complex geological history resulted in a highly differentiated subsurface structure. Elongated basement highs and narrow depressions developed during the Mid-Miocene rifting (ROYDEN & HORVÁTH, 1988) were refigured by several phases of basin inversion prior to, during and after the subsequent thermal subsidence (PRELOGOVIĆ et al., 1998; TOMLJENOVIĆ & CSONTOS, 2001). Most of the sedimentary succession accumulated in these depressions which are separated by uplifted and partially eroded tectonic units. The mentioned depressions – the most northern Mura depression, Drava depression, Sava depression and Slavonija-Srijem depression are filled with the Neogene rocks. Some of the basement highs are exposed as Palaeozoic-Mesozoic mountains (e.g. Mt. Papuk, Mt. Psunj etc.) while others are still covered by 1000-2000 m thick Neogene and Quaternary sediments.

Generalised stratigraphic column of the southern Pannonian basin is given in Fig 2-1. Basin fill contains some volcaniclastics (and volcanic rocks as well) but is mostly composed of sediments reaching maximal thickness of e.g. 5000 m in Sava depression or over 6000 m in Drava depression. The oldest Neogene sediments are of Early to Middle Miocene age and comprise syn-rift and early post-rift sediments (SAFTIĆ et al. 2003). Terrestrial sandstones, subordinate coal seams, sedimentary bodies of talus breccia (mainly Lower Miocene), reefs (mainly Badenian), coastal and shallow marine sandstones (Karpatian, Badenian) are interlayered with volcaniclastics/volcanics, marls and clayey limestones. The end of Middle Miocene is characterised mostly by fine-grained deposition in the starving brackish-water basin. Late Miocene age is characterised by the post-rift thermal subsidence of the Pannonian basin (SAFTIĆ et al., 2003). Lake Pannon deposits were formed in brackish (Pannonian) to freshwater environment (Pontian). Apart from local variations due to pre-Pannonian topography the sedimentary succession begins with littoral limestones and nearshore transgressive lag overlain by hemipelagic calcareous and clayey marls basin-wide. The deepest depressions were filled by lacustrine turbidite lobes and channel fills of considerable thickness, thus initial basin floor topography gradually became levelled. Turbiditic successions are overlain by shale-prone delta slope and sandy delta front to coastal plain sediments.

| Fig.2-1. Stratigraphic column of the Neogene basin fill of southern Pannonian basin | Fig. 2-2. Stratigraphic column of the northern Adriatic offshore |
| --- | --- |

Pliocene and Quaternary rocks are sediments which were deposited in the remnants of Lake Pannon and in the subsequent fluvial systems (SAFTIĆ et al., 2003). These are mostly sands and sandy gravels with some clay and silt that have the largest thickness of 1000-1500 m in areas of continuous subsidence (Fig. 2-1). At that time Lake Pannon occupied only the southernmost part of the Pannonian basin. The largest number of oil and gas reservoirs was found in the Upper Miocene sandstones interlayered with silty marls, but the largest single reservoirs were much deeper, either in the Lower to Middle Miocene coarse clastic bodies, or in the Mesozoic and Palaeozoic basement rocks.

Adriatic offshore  The oldest rocks reached by wells in the Adriatic offshore are of Permian age. They are of heterogeneous lithologic composition – mainly sandstone and shale, but carbonate formations are also present, and particularly evaporites. Lower Triassic sequence consists of both siliceous and carbonaceous sandstones with subordinated tuff and dolomite indicating shallow water conditions. Middle Triassic unit was affected by the beginning of the Alpine orogenesis and both the shallow water and deep water carbonates are found, frequently with andesite and pyroclastics. In the Late Triassic dolomites prevail in the Northern Adriatic. Generally, shallow water carbonate sedimentation (mainly dolomites) in platform conditions began in Late Triassic and continued in more-less similar platform conditions throughout Jurassic and Cretaceous, till the Palaeogene or occasionally Middle Eocene. Towards the end of Cretaceous the platform gradually disintegrated. The thickness of carbonate deposits amounts to 5000 m at most. During the Middle Eocene, Late Eocene and Lower Oligocene, tectonic movements caused opening of the future Adriatic basin (PRELOGOVIĆ & KRANJEC, 1983). The movements were accompanied by sedimentation of marl, sandstone and subordinated limestone. Miocene was characterised by hemipelagic marl in the central parts of deep basins and turbidites close to their margins – marl, calcareous and marly siltites interbedded with sandy limestones and sandstones. Pliocene sediments resulting from the subsequent transgression include clays, marls and sands. There is a lithologic continuity with Quaternary deposits composed of sands, silts and clays with lignite interbeds. Thickness of Pliocene-Quaternary sequence in the Northern Adriatic reaches 1000 m.

Several gas fields were discovered in the Northern Adriatic with reservoirs within Pliocene-Quaternary deposits. Traps were formed by differential compaction resulting in small structural closures and there are numerous isolated sand bodies. They are characterised by intergranular porosity and markedly irregular distribution of reservoir properties (ZELIĆ et al., 1999). Few reservoirs were also discovered in the underlying karstified Upper Cretaceous carbonates.

2.3 Prospective geological storage objects

Most of the regional studies indicate that sedimentary basins worldwide could offer significant storage potential and Croatian territory is no exception. Coal layers in Croatia are both too shallow or to thin to result in significant storage potential and it is best to direct attention to the other two types – depleted oil and gas reservoirs and deep saline aquifers.

In the Pannonian basin, EOR pilot studies are on the way and it is to be expected that the first industrial CO2 injection will be done in order to increase the production of oil from the two depleted fields. The so far obtained results (DOMITROVIĆ et al., 2005) prove that it can be done and that significant proportion of injected CO2 will remain in the reservoir permanently. In the southern Pannonian basin (Fig. 2-1), Upper Miocene sandstones are the most frequent type of reservoir rocks that might be used because they are numerous, reliably correlated and usually in the convenient depth range (1000-2500 m). At some locations, large capacity is estimated in the Base Neogene breccia-conglomerate bodies, and particularly where those reservoirs are hydraulically connected with the underlying Mesozoic or Palaeozoic rocks. To construct underground carbon storages in these reservoirs might prove to be complicated due their large depths and consequently high pressure and temperature, and the extensively developed fracture porosity. As for the off-shore possibilities, only northern and central Adriatic are geographically/economically reachable and three types of reservoirs are worth investigating – Pliocene/Quaternary sands/sandstones that are documented to be gas-tight but these gas pools are either too shallow or at the marginal depth (750-850 m), Upper Cretaceous limestones with secondary porosity covered with impermeable Miocene or Pliocene sediments and Miocene formation that is locally developed between the first two, especially in the deep depressions like the Dugi Otok basin (Fig. 2-3).

Fig. 2-3. Major aquifers, oil and gas fields and pipelines in Croatia

Calculations (capacity estimates) were performed for altogether 15 fields in the Pannonian basin and 3 fields in the Northern Adriatic off-shore. Locations are given in Fig. 2-3. The capacity was calculated based on the volume of the already produced hydrocarbons, considering that all of it can now be safely filled with pure CO2. The listed capacity in gas fields (Table 2-1) greatly exceeds the one in oil fields, but gas fields are still far from depletion and will not be converted to storages very soon. As for the oil fields, the obtained total capacity is approximately 5 times smaller, but at least some among them are “ready to be used”, firstly for EOR and subsequently for permanent CO2 storage. Their geographical distribution is favourable – close to the major point sources in continental Croatia (Fig. 2-3) and only limiting factors are seen in the size of their reservoirs and occasionally large number of old wells that will have to be plugged and monitored.

Table 2-1. Estimates of storage capacity in hydrocarbon fields

| Basin (no. of fields) | Stratigraphic unit | Lithological composition | Depth (m) | Capacity (Mt) |
| --- | --- | --- | --- | --- |
| Drava (2) | Miocene | carbonate breccia/ sandstone | 1950/750 | 12.3 |
| Sava (5) | Miocene/Palaeozoic | sandstone/ granite | 1580-825 | 23.2 |
|  | ( Oil fields | 35.5 |
| Drava-deep (4) | Miocene/ Mesozoic/ Palaeozoic | breccia/ carbonates/ metamorphic rocks | 3200-900 | 83.15 |
| Drava-shallow (2) | Miocene | sandstone | 1600 | 17.75 |
| Sava (2) | Miocene | sandstone | 2000-1850 | 20.2 |
| N. Adriatic (3) | Quaternary/Pliocene/ Mesozoic | sand/ sandstone/ carbonates | 900/1300 | 32.1 |
|  | ( Gas fields | 153.2 |
|  | (( | 188.7 |

To estimate the capacity in deep saline aquifers, presents a problem due to the lack of detailed data. Even in the mature petroleum provinces deep aquifers were simply not drilled through enough and there are just a few analyses of their reservoir properties. That is why even in the cases where the geometry of the reservoir rock formations can be delineated based on the regional subsurface data, other parameters – effective thickness, porosity, temperature have to be estimated. This inevitably puts in a lot of uncertainties. The adequate trapping conditions in parts of these regional aquifers will only later be confirmed by targeted surveys. That is why these storage estimates are regarded as theoretical capacity only and are usually declared as the total pore space volume to make it clear that only part of it can eventually be used for CO2 storage. Pore space volume listed in Table 2-2 is actually total pore space volume multiplied by a displacement coefficient which is only roughly estimated to be 3%, meaning that only such a small proportion of available pores might probably once be filled with carbon dioxide (at several locations that are still to be chosen and explored in detail). In conclusion, if the estimated cumulative volume within aquifers is multiplied with CO2 density at average depth and temperature, which is 500 kg/m3 it sums up to 4829 Mt which is far more than estimated in the oil and gas fields. This capacity might be prepared for use only after the deliberated exploration of these objects to fully investigate their reservoir properties, and to confirm the integrity of their cap rocks.

Table 2-2. Estimates of theoretical storage capacity in deep saline aquifers

| Aquifer | Area (m2) | Depth Top (m) | Depth Base (m) | H (m) | Hef (m) | Porosity | Pore space volume (m3) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dugi Otok | 1135546278 | 930 | 2100 | 1170 | 234 | 0.1 | 797153487 |
| Drava | 1353234016 | 900 | 1900 | 1000 | 600 | 0.25 | 6089553071 |
| Osijek | 41085959 | 1000 | 3500 | 2500 | 1750 | 0.2 | 431402566 |
| Sava West | 314735506 | 800 | 2300 | 1500 | 500 | 0.17 | 802575539 |
| Sava Central | 517134191 | 1000 | 2700 | 1700 | 550 | 0.18 | 1535888547 |
|  | (( | 9656573210 |

3. Conclusions and recommendations

Several conclusions can be drawn based on the explained screening. Failing to consider those carefully might significantly impair future development of the energy sector:

- Croatia will be very soon facing the challenge of reducing CO2 emissions. One of the ways to achieve significant reductions on a national level is to equip large industrial stationary sources with adequate capturing facilities, and to build a transport system capable of safely conveying CO2 streams to the geological storage objects situated deep in the subsurface (under 1000 m).

- There are favourable natural conditions for geological storage of carbon dioxide in some parts of Croatia – in the southern Pannonian basin, and in the Adriatic off-shore as well. It is also important that significant human and technical resources of the national oil industry can be fully used to that purpose.

- The most prospective objects in the near future are the depleted hydrocarbon fields but in the long term, oil and gas reservoirs will not offer the largest capacity. There are two reasons for that. The first is that old oil fields usually have a large number of old wells drilled through the reservoirs, and those wells significantly increase the risk of leakage to the atmosphere or at least cause additional costs for plugging and monitoring. The other reason is even more obvious – since the prices of crude oil are so high the remaining reserves in partly depleted reservoirs are so valuable that this hinders the large-scale utilisation of oil and gas reservoirs for any other purpose except additional extraction.

- Significantly larger capacity is estimated in the deep saline aquifers – porous and permeable regional formations deeper than 1000 m. There should be no conflict of use to define and equip underground storage sites in a part of this waste pore space, but the subsurface data available are too scarce to allow anything but generalised regional estimates to be made. That is why it will be necessary to develop research projects targeted specifically to the better definition of their geological composition and reservoir properties.

The preparations will have to be really quick in order to fully develop the carbon capture and storage system in time to achieve significant reduction of CO2 emissions. In light of the international commitments made by Croatia, this could really have grave impact on the price of energy in the near future. Also, there is a potential benefit of improving one country’s image as an economy that uses its fossil energy sources in environmentally friendly way.

Acknowledgements

This research was enabled by participating in the two EU FP6 projects – CASTOR and EU GeoCapacity. Authors greatly appreciate the support from the Croatian side that came through the Environmental Protection and Energy Efficiency Fund and from the Croatian power supply company HEP.

REFERENCES

BACHU, S.: Sequestration of CO2 in geological media: criteria and approach for site selection in response to climate change, Energy Conversion & Management, (2000), 41, pp. 953-970.

BACHU, S.: Screening and ranking of sedimentary basins for sequestration of CO2 in geological media in response to climate change, Environmental Geology, (2003), 44, pp. 277-289.

CSLF (2007): Phase II Final Report from the Task Force for Review and Identification of Standards for CO2 Storage Capacity Estimation (http://www.cslforum.org/documents/PhaseIIReportStorageCapacityMeasurementTaskForce.pdf)

DOMITROVIĆ D., ŠUNJERGA S., GORIČNIK B., VULIN D.: Simulation study of CO2 retention during tertiary EOR flood In Ivanić oilfield, EAGE 67th Conference & Exhibition — Madrid, Spain, 13 - 16 June 2005, Z-99

EKONERG: National inventory report for the period 1990-2003, prepared for Ministry of Environmental Protection, Physical Planning and Construction, July 2005

IPCC (2005): IPCC Special Report on Carbon dioxide Capture and Storage (http://www.ipcc.ch/ipccreports/srccs.htm)

PACALA, S. & SOCOLOW,R.: Stabilization Wedges: Solving the Climate Problem for the Next 50 Years with Current Technologies, Science, 305 (2004), pp. 968-972.

PRELOGOVIĆ E. & KRANJEC V.: Geološki razvitak područja Jadranskog mora (in Croatian), Pomorski zbornik 21 (1983), pp. 387-405

PRELOGOVIĆ E., SAFTIĆ B., KUK V., VELIĆ J., DRAGAŠ M. & LUČIĆ D.: Tectonic activity in the Croatian part of the Pannonian basin, Tectonophysics, 297 (1998), pp. 283-293

ROYDEN L. H. & HORVÁTH F. (eds.): The Pannonian Basin – A Study in Basin Evolution, AAPG Memoir, 45 (1988), 394 p

SAFTIĆ B., VELIĆ J., SZTANÓ O., JUHÁSZ Gy. & IVKOVIĆ Ž.: Tertiary subsurface facies, source rocks and hydrocarbon reservoirs in the SW part of the Pannonian Basin (northern Croatia and south-western Hungary), Geologia Croatica, 56/1 (2003), pp. 102-122

TOMLJENOVIĆ B. & CSONTOS L.: Neogene-Quaternary structures in the border zone between Alps, Dinarides and Pannonian Basin (Hrvatsko zagorje and Karlovac Basins, Croatia), Int. J. Earth. Sci., 90 (2001), pp. 560-578

ZELIĆ M., MLINARIĆ Ž. & JELIĆ-BALTA J.: Croatian Northern Adriatic Ivana gas field ready for development (Reservoir characteristics and gas inflow conditions into the well), Nafta, 50, 1 (1999), pp. 19-37

Vraćanje ugljikova dioksida u podzemlje – mogućnosti u Hrvatskoj

Sažetak: Hvatanje i geološko uskladištenje ugljikova dioksida predstavlja mogućnost za sprečavanje ispuštanja ovog stakleničkog plina u atmosferu. Proces uključuje izdvajanje ugljikova dioksida iz dimnih plinova velikih stacionarnih izvora, transport plinovodima ili brodovima i utiskivanje duboko u podzemlje. Primjena sustava za hvatanje i uskladištenje ugljika mogla bi pomoći Hrvatskoj u ostvarivanju ograničenja postavljenih Protokolom iz Kyota. U južnom dijelu Panonskog bazena i u podmorju Jadrana postoje formacije propusnih stijena s povoljnim uvjetima za izgradnju podzemnih skladišta ugljika. Izgledno je da će prvi kandidati za to biti dobrim dijelom iscrpljena naftna i plinska polja, osobito naftna polja na kojima su započete operacije povećanja iscrpka nafte korištenjem ugljičnog dioksida kao utisnog fluida, no značajno veći potencijal za uskladištenje u budućnosti imaju duboki slani vodonosnici regionalnog pružanja.

Ključne riječi: hvatanje i geološko uskladištenje ugljika (CCS), kapacitet geološkog skladištenja, iscrpljena naftna i plinska ležišta, duboki slani vodonosnici, Panonski bazen, podmorje Jadrana, Hrvatska.