UNIVERSITY OF ZAGREB FACULTY OF MECHANICAL ENGINEERING AND NAVAL ARCHITECTURE DEPARTMENT OF NAVAL ARCHITECTURE AND OFFSHORE ENGINEERING IVANA LUČIĆA 5, 10000 ZAGREB , CROATIA TEL +385 1 6168 222 FAX +385 1 6156940

TECHNICAL REPORT

Title of Report : ANALYSIS OF HARBOUR PONTOON(BARGE) STRUCTURE

Report no. : USCS/HELIYACHTS Report .No. BARGE 1

Date : March 2000

Client / Sponsor : USCS/ HELIYACHTS Internationl, Pula, CROATIA fax : (052) 216 161

Work carried out by : Dr Vedran Žanić, Dipl.ing.Tomislav Jančijev, Dipl.ing.Jerolim Andrić

Approved by : Dr Vedran Žanić TEL +385 1 6168 122 ; E-mail vedran.zanic@fsb.hr Dipl.ing.Tomislav Jančijev

Summary : The objective of the analysis is to investigate the structural strength of the harbor barge with carrying capacity 750 t in fulfillment of requirements for direct calculation of the classification societies Lloyds Register. Full dock 3D FEM MAESTRO model was generated in accordance with LR Rules and Regulations for the Construction and Classification of Floating Docks, January 1987 , supplied by the Builder. Finite element model contains 2668 nodes ( 16008 degrees of freedom), 1292 finite macroelements (92 girders, 648 stiffened panels, 386 transverse beams, 32 pillars, 124 additional beams, and 10 triangles) Seven static load cases, supplied by the Builder, were generated using given weight and ballast distribution for 500 t yachts carried by WISE MARINE HOIST on four legs adjusted to the longitudinal weight distribution from the corresponding hydrostatic calculation. This report describes recommendations for change of scantlings based on 3D MAESTRO FEM calculations. New scantlings are given in the enclosed Figures 1- 4.

Key words : Barge, pontoon, finite elements, MAESTRO modeling,