UNIVERSITY OF ZAGREB FACULTY OF MECHANICAL ENGINEERING AND NAVAL ARCHITECTURE DEPARTMENT OF NAVAL ARCHITECTURE AND OFFSHORE ENGINEERING IVANA LUČIĆA 5, 10000 ZAGREB , CROATIA TEL +385 1 6168 222 FAX +385 1 6156940

TECHNICAL REPORT

Title of Report : ANALYSIS OF HARBOUR FLOATING DOCK STRUCTURE (600 m.t. Lifting capacity)

Report no. : USCS/HELIYACHTS Report .No. DOCK 1

Date : January 2000

Client / Sponsor : USCS/ HELIYACHTS Internationl, Pula, CROATIA fax : (052) 510 011 (local 6)

Work carried out by : Dr Vedran Žanić, Dipl.ing.Tomislav Jančijev, Dipl.ing.Jerolim Andrić

Approved by : Dr Vedran Žanić TEL +385 1 6168 122 ; E-mail vedran.zanic@fsb.hr Dipl.ing.Tomislav Jančijev

Summary : The objective of the analysis was to investigate the structural strength of the harbor floating dock with lifting capacity 600 t in fulfillment of requirements for direct calculation of the classification societies Croatian Register of Shipping and Lloyds Register. Full dock 3D FEM MAESTRO model was generated in accordance with LR Rules and Regulations for the Construction and Classification of Floating Docks, January 1987 , supplied by the Builder. Ten static load cases, supplied by the Builder, were generated using given weight and ballast distribution for (1) 200 t yachts carried by WISE MARINE HOIST and (2) 600 t ships carried on four axle carriage adjusted to the longitudinal weight distribution from the corresponding hydrostatic calculation. This report describes recommendations for change of scantlings based on 3D MAESTRO FEM calculations. New scantlings are given in the enclosed Figures 1- 4.

Key words : Floating dock, finite elements, MAESTRO modeling,