UNIVERSITY OF ZAGREB FACULTY OF MECHANICAL ENGINEERING AND NAVAL ARCHITECTURE DEPARTMENT OF NAVAL ARCHITECTURE AND OFFSHORE ENGINEERING IVANA LUČIĆA 5, 10000 ZAGREB , CROATIA TEL +385 1 6168 222 FAX +385 1 6156940

TECHNICAL REPORT

Title of Report : HULL STRUCTURE ANALYSIS OF BULK CARRIER-PROJECT 972

Report no. : SPT1-PROJECT 972

Date : March 2000

Client / Sponsor : BRODOSPLIT Shipyard, SPLIT, CROATIA

Work carried out by : Dr Vedran Žanić, Dipl.ing.Tomislav Jančijev, Dipl.ing.Jerolim Andrić

Approved by : Dr Vedran Žanić TEL +385 1 6168 122 ; E-mail vedran.zanic@fsb.hr Dipl.ing.Tomislav Jančijev NOT APPROVED

Summary : The objective of the analysis is to investigate the structural strength of the 3-hold model of the bulk carrier 51 000 TDW (project 972) in fulfillment of requirements for direct calculation of the classification society American Bureau of Shipping (ABS). 3D FEM MAESTRO model for critical structural holds is generated in accordance with ABS safety factors and recommendations. 3D FEM model has approximately 77 570 DOF and 9340 macro- elements. Two test loadcases : LC1=ABS LC1,but with ballast in hold no.3 LC2= ABS LC4, but with liquid in holds no. 5 and 3 (s.g.=1.5) are generated using given weight distribution and adjusted to the required bending moment distribution from the corresponding hydrostatic calculation. This report describes the preliminary results (stresses and adeqacy parameters) obtained. Safety factor gama is calculated from the normalised safety factor g presented in Figures 1-16 : gama = K * (1+g) / (1-g); K = 1.18 (PCCB, PCSF), K=1.11 (PFLB), K=2 (FCPH) e.g g = - 0.2 --- > gama (PCCF) = 0.78 Mnemonics of PCCB, PCSF, etc. are referenced in RO-PAX Report. Final decisions about structure can only be made after completing analysis for all loadcases required and approved by ABS.

Key words : Bulk carrier, finite elements, MAESTRO modeling,