UNIVERSITY OF ZAGREB FACULTY OF MECHANICAL ENGINEERING AND NAVAL ARCHITECTURE DEPARTMENT OF NAVAL ARCHITECTURE AND OFFSHORE ENGINEERING IVANA LUČIĆA 5, 10000 ZAGREB , CROATIA TEL +385 1 6168 222 FAX +385 1 6156940

TECHNICAL REPORT

Title of Report : FINE MESH ANALYSIS OF FLOOR OPENINGS IN BULK CARRIER (PROJECT 972)

Report no. : SPT 5-PROJECT 972

Date : November 2000

Client / Sponsor : BRODOSPLIT Shipyard, SPLIT, CROATIA

Work carried out by : Dr Vedran Žanić, Dipl.ing.Tomislav Jančijev, Dipl.ing. Darko Frank, Dipl.ing.Jerolim Andrić

Approved by : Dr Vedran Žanić TEL +385 1 6168 122 FAX 6168 399; E-mail vedran.zanic@fsb.hr Dipl.ing.Tomislav Jančijev

Summary : BRODOSPLIT shipyard has contracted University of Zagreb (UZ), Faculty of Mech. Eng. and Naval Arch. to perform 3D FEM analysis of Yard 972 using MAESTRO software available at University of Zagreb. The objective of the analysis is to investigate the structural strength of the 3-hold model of the bulk carrier 51 000 TDW (project 972) in fulfillment of requirements for direct calculation of the classification society American Bureau of Shipping (ABS). 3D FEM MAESTRO model for critical structural holds is generated in accordance with ABS safety factors and recommendations. 3D FEM model has approximately 77 570 DOF and 9340 macro- elements. Nine loadcases : LC1-LC9 from ABS Rules are generated using given weight distribution and adjusted to the required bending moment distribution. The details are covered in Report SPT 2-PROJECT 972 (May 2000). The Report SPT 4-PROJECT 972 (September 2000) describes global model usage in providing boundary conditions for fine mesh analysis of floors in double bottom structure. Critical values of shear and von Mises stresses in global analysis are obtained at Fr 128 in ABS loadcases 2 and 4 . 3D fine mesh model for Detail Stress Analysis (DSA) using "top down approach" is developed (Fr 127-129, 70296 DOF, 11716 Q4 shell element groups). The displacement boundary conditions are automatically transferred from the MAESTRO global model to DSA models as well as local loads. High stress areas are clearly identified in global and DSA model. Structural modifications (stiffening) are suggested. Model, boundary conditions and permmited stress levels are adjusted to ABS requirements. This report covers the results of Detail Stress Analysis (DSA) of the critical floors from the Report SPT 4-PROJECT 972 for Yard required modifications. Modifications include closing of openings between longitudinals 8 – 9 and 10-11 and collar stiffening of holes between stiffeners 7-8 and 11-12. Obtained von Mises and shear stress levels are presented in Figs 1-4. They are at ABS permited levels for material grades applied.

Key words : Bulk carrier, finite elements, MAESTRO modeling,

A P P E N D I X

FIG. 1-4

| REPORT no.: 5 | SUBJECT: Plot of von Mises Stresses for LC2 | FIGURE: 1 |
| --- | --- | --- |
| BRODOSPLIT BULK CARRIER - Project 972 |  |  |
|  | UNIVERSITY OF ZAGREB Faculty of Mechanical Engineering and Naval Architecture |  |
| DATE: September 2000 |  |  |

| REPORT no.: 5 | SUBJECT: Plot of von Sheer Stresses for LC2 | FIGURE: 2 |
| --- | --- | --- |
| BRODOSPLIT BULK CARRIER - Project 972 |  |  |
|  | UNIVERSITY OF ZAGREB Faculty of Mechanical Engineering and Naval Architecture |  |
| DATE: September 2000 |  |  |

| REPORT no.: 5 | SUBJECT: Plot of von Mises Stresses for LC4 | FIGURE: 3 |
| --- | --- | --- |
| BRODOSPLIT BULK CARRIER - Project 972 |  |  |
|  | UNIVERSITY OF ZAGREB Faculty of Mechanical Engineering and Naval Architecture |  |
| DATE: September 2000 |  |  |

| REPORT no.: 5 | SUBJECT: Plot of Shear Stresses for LC4 | FIGURE: 4 |
| --- | --- | --- |
| BRODOSPLIT BULK CARRIER - Project 972 |  |  |
|  | UNIVERSITY OF ZAGREB Faculty of Mechanical Engineering and Naval Architecture |  |
| DATE: September 2000 |  |  |