UNIVERSITY OF ZAGREB FACULTY OF MECHANICAL ENGINEERING AND NAVAL ARCHITECTURE DEPARTMENT OF NAVAL ARCHITECTURE AND OFFSHORE ENGINEERING IVANA LUČIĆA 5, 10000 ZAGREB , CROATIA TEL +385 1 6168 222 FAX +385 1 6156940

TECHNICAL REPORT

Title of Report : HULL STRUCTURE ANALYSIS OF BULK CARRIER-PROJECT 972 DOUBLE BOTTOM DESIGN - PARAMETRIC STUDY

Report no. : SPT 3-PROJECT 972

Date : July 2000

Client / Sponsor : BRODOSPLIT Shipyard, SPLIT, CROATIA

Work carried out by : Dr Vedran Žanić, Dipl.ing.Tomislav Jančijev, Dipl.ing.Jerolim Andrić

Approved by : Dr Vedran Žanić TEL +385 1 6168 122 ; E-mail vedran.zanic@fsb.hr Dipl.ing.Tomislav Jančijev

Summary : Parametric study w.r.t. the number and spacing of longitudinals in double bottom structure of bulk carrier-project 972 is performed at the request of the Yard. Botom girder position is changed due to modifications in number of longitudinals between them. Three bottom structure variants supplied by the Yard (PROPOSAL 1, PROPOSAL 2 and PROPOSAL 3) are investigated. 3D FEM MAESTRO model of each variant for the critical structural holds is generated in accordance with ABS recommendations. 3D FEM model has approximately 77 570 DOF and 9340 macro- elements. Four hogging loadcases : LC2, 4, 6 and 8 from ABS Rules are generated using given weight distribution and adjusted to the required bending moment distribution. This report describes results (stresses and adequacy parameters) obtained after completing analysis for specified loadcases for all three structural variants. Results enabling selection of optimal structural layout for double bottom are given.

Key words : Bulk carrier, finite elements, MAESTRO modeling, parametric study of double bottom

CONTENTS									PAGE

1. SCOPE  OF THE PARAMETRIC STUDY	                                        	1 - 1

2. RESULTS OF THE PARAMETRIC STUDY                                                     2 - 1

3. CONCLUSIONS                                                                                                  3 - 1

APPENDIX A:           FIGURES

TABLES

DIAGRAMS

APPENDIX B:           STRUCTURAL EVALUATION; SUMMARY OF FAILURE TYPES

FIGURE DESCRIPTION					                                               FIGURE NO.

GENERAL

3-D View of Undeformed Full  F.E.M Model - Prototype                                                          	                          1

3-D View of Undeformed Half   F.E.M Model - 						            	            2

Midship Section Geometry             									            3

Sketch of 3 type of double bottom topology                  						            4

PROPOSAL -1 RESULTS:

3-D Plot of (x Stresses of Stiffened Panels for LC2-bottom structure /middle hold                                                      5

3-D Plot of (x Stresses of Stiffened Panels for LC4-bottom structure /middle hold                                                      6

3-D Plot of (x Stresses of Stiffened Panels for LC6-bottom structure /middle hold                                                      7

3-D Plot of (x Stresses of Stiffened Panels for LC8-bottom structure /middle hold                                                      8

3-D Plot of (y Stresses of Stiffened Panels for LC2-bottom structure /middle hold                                                      9

3-D Plot of (y Stresses of Stiffened Panels for LC4-bottom structure /middle hold                                                    10

3-D Plot of (y Stresses of Stiffened Panels for LC6-bottom structure /middle hold                                                    11

3-D Plot of (y Stresses of Stiffened Panels for LC8-bottom structure /middle hold                                                    12

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view under D0                         13

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view above D1                        14

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view without D1                      15

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC2                                                              16

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC2                                                             17

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC2                                                              18

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC2                                                             19

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC4                                                              20

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC4                                                             21

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC4                                                              22

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC4                                                             23

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC6                                                              24

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC6                                                             25

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC6                                                              26

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC6                                                             27

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC8                                                              28

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC8                                                             29

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC8                                                              30

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC8                                                             31

PROPOSAL - 2  RESULTS:

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view under D0                         32

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view above D1                        33

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view without D1                      34

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC2                                                              35

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC2                                                             36

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC2                                                              37

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC2                                                             38

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC4                                                              39

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC4                                                             40

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC4                                                              41

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC4                                                             42

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC6                                                              43

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC6                                                             44

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC6                                                              45

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC6                                                             46

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC8                                                              47

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC8                                                             48

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC8                                                              49

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC8                                                             50

PROPOSAL - 3  RESULTS:

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view under D0                         51

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view above D1                        52

3-D Plot of Worst Normalized Safety Factors on Stiffened Panels for all loadcases- view without D1                      53

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC2                                                              54

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC2                                                             55

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC2                                                              56

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC2                                                             57

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC4                                                              58

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC4                                                             59

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC4                                                              60

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC4                                                             61

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC6                                                              62

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC6                                                             63

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC6                                                              64

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC6                                                             65

3-D Plot of  PCSF Normalized Safety Factors on Stiffened Panels for  LC8                                                              66

3-D Plot of  PYCF Normalized Safety Factors on Stiffened Panels for  LC8                                                             67

3-D Plot of  PFLB Normalized Safety Factors on Stiffened Panels for  LC8                                                              68

3-D Plot of  PCCB Normalized Safety Factors on Stiffened Panels for  LC8                                                             69

TABLES

TABLE 1:               Load case description

TABLE 2:               Adequacy parameter values for PROPOSAL 1

TABLE 3:               Adequacy parameter values for PROPOSAL 2

TABLE 4:               Adequacy parameter values for PROPOSAL 3

TABLE 5:               Parametric study of safety factors in botttom plating strakes (strakes no.1 ,2, 3, 4-see Fig 3)

TABLE 6:               Parametric study of safety factors in all double botttom plating strakes

TABLE 7:               Constraint per range interval

TABLE 8:               Summary of decision making data

DIAGRAMS

Diagram 1:               Comparison of bottom plating strakes

Diagram 2:               Comparison of all strakes in double bottom structure

Diagram 3 :	  Histogram of normalized safety factors for all strakes of double bottom structure

1. SCOPE  OF THE PARAMETRIC STUDY

1.1  GENERAL

Ship detailed description is given in the previous Report SPT 2-PROJECT 972

General 3-D view of 3-Hold FEM model is given in Figs. 1 and 2.

Midship section geometry with strake numbering is given in Fig. 3

Three bottom structure variants supplied by the Yard  (PROPOSAL 1, PROPOSAL 2 and

PROPOSAL 3) are presented in Fig.4 based on Yard fax of 14.07.2000.

Objective of the study is to investigate optimal layout of stiffeners and girder position in double bottom based primarily on buckling criteria.

Proposals are based on PROTOTYPE dimensions from Report SPT 2-PROJECT 972 but four

bottom plating strakes are given common plate thickness of 20 mm instead of 15 mm due to buckling

recorded on PROTOTYPE.

All thickness is taken without corrosion addition with respect to any response and safety analysis.

Four  hogging loadcases : LC2, 4, 6 and 8  from ABS Rules are generated using given weight distribution and adjusted to the required bending moment distribution.They are summarized in the Table 1.

2. RESULTS OF THE PARAMETRIC STUDY

3D FEM MAESTRO model of each variant for the critical structural holds is generated in accordance with  ABS  recommendations.

3D FEM model has approximately  77 570 DOF and 9340 macro- elements.

Obtained stresses for specified loadcases for double bottom strakes of  PROPOSAL 1 are given in Figs 5 - 12.

Structural adequacy is checked using library of failure criteria in-built in MAESTRO.

For the purpose of the presentation of results the strength ratio R is defined as follows:

R(X) = Q(X) /QL(X)

where X is vector of current values of structural parameters including scantlings,

Q( ) is load effect and QL( ) is its limit value for particular failure mode. Failure

criterion is given by :

( R(X) < 1

or in normalized form using  ‘adequacy parameter’ g(R):

g(R) > 0      where       g(R) = (1-( R) / (1+( R)  and   -1<g<1

Safety factors (() used in constraints are set to 1 since the degree the structure (i. e. double bottom) has suffered some type(s) of failures of collapse or serviceability (see 1, page 4-6).

Worst recorded values of normalized safety factors (g) for stiffened panels of PROPOSAL 1 are given in Figs. 13 - 15.

Most unsatisfied criteria PCSF , PYCF, PFLB and PCCB for all specified load cases are given in Figs .16 - 31.

Worst recorded values of normalized safety factors (g) for stiffened panels of PROPOSAL 2 are given in Figs. 32 - 34.

Most unsatisfied criteria PCSF , PYCF, PFLB and PCCB for all specified load cases are given in Figs .35 - 50.

Worst recorded values of normalized safety factors (g) for stiffened panels of PROPOSAL 3 are given in Figs. 51 - 53.

Most unsatisfied criteria PCSF , PYCF, PFLB and PCCB for all specified load cases are given in Figs .54 - 69.

Summary of recorded adequacy parameters for bottom strakes in PROPOSAL 1, 2 and 3 are given in Tables 2 - 4.

Following information needed for decision on optimal layout of double bottom longitudinals is given in the Tables 5, 6, 7 and 8 :

MEAN values, STDEV (standard deviation)  and C.O.V (coefficient of variation = STDEV / MEAN) of  normalized safety factors for each bottom strake (PS and SB) are given  in two last columns .

MEAN values, STDEV  and C.O.V of  normalized safety factors for each criterion (mnemonics see Appendix B) are given  in rows 2, 3, and 4.

Overall  MEAN, STDEV and C.O.V. for entire double bottom are given in upper right corner  of the Tables.

Last row of the tables contain MINimum value of each constraint recorded for double bottom.

3. CONCLUSIONS

Data presented for the selection of the optimal longitudinals layout in the double bottom structure is  given in Table 5 (bottom plating) and Table 6 ( entire double bottom structure) are as follows  :

NoNEG  - number of unsatisfied criteria in the  structure

MIN g    - worst recorded unsatisfied value of norm. safety criterion.

Rel.A.I.  - relative adequacy index. It is defined as:

Apos

Rel. A.I.  =  --------------------

Apos + Aneg

where Apos is the area under the distribution of positive values of g, and Aneg is the area under the distribution of negative values taken from histograms for PROPOSALS 1, 2, and 3. Histogram (DIAGRAM 3) presents the number of criteria satisfied  within each specified range (see Table 7).

Graphic presentation of criteria satisfaction are given in diagrams 1 and 2.

Considering of bottom plating all three proposals have almost the same number of NoNEG but proposals 2 and 3 are superior in satisfaction of constraints and better Rel. A. I. PROPOSAL 3 has the worst unsatisfied constraint value (MIN g) but the smallest Aneg. PROPOSAL 3 has best Rel.A.I.

When the whole double bottom is analyzed PROPOSAL 2 is superior to PROPOSAL 3 in buckling criteria (PCSF, PCCB, PFLB and PCSB) and MIN g.. PROPOSAL 3 has best Rel.A.I. as the MAESTRO overall measure of structural adequacy.

REFERENCES

- MAESTRO Version 8.024 , Program documentation, Proteus engineering, Stensville, MD, USA

- O. F. Hughes: Ship Structural Design, John Wiley & Sons, Inc. 1983.

- O.F. Hughes, F. Mistree, V.Žanić : A Pratical Method for the Rational Design of Ship Structures, Journal of Ship Research, 24, 1980.

TABLE 7: Constraint per range interval

| RANGE | PROP 1 | PROP 2 | PROP 3 |
| --- | --- | --- | --- |
| -1 | 0 | 0 | 0 |
| -0,9 | 0 | 0 | 0 |
| -0,8 | 0 | 0 | 0 |
| -0,7 | 0 | 0 | 0 |
| -0,6 | 0 | 0 | 1 |
| -0,5 | 0 | 0 | 2 |
| -0,4 | 2 | 3 | 0 |
| -0,3 | 6 | 1 | 3 |
| -0,2 | 7 | 10 | 7 |
| -0,1 | 16 | 10 | 10 |
| -0,01 | 18 | 24 | 25 |
| 0 | 0 | 1 | 3 |
| 0,01 | 1 | 0 | 0 |
| 0,1 | 12 | 8 | 10 |
| 0,2 | 17 | 20 | 21 |
| 0,3 | 24 | 22 | 20 |
| 0,4 | 13 | 16 | 14 |
| 0,5 | 24 | 22 | 24 |
| 0,6 | 31 | 32 | 22 |
| 0,7 | 16 | 18 | 22 |
| 0,8 | 9 | 11 | 10 |
| 0,9 | 6 | 4 | 7 |
| 1 | 84 | 84 | 85 |
| Ntot | 286 | 286 | 286 |

TABLE 8: Summary of decision making data

| CONSTRAINT AREA CHAR. |  |  | PROP 1 | PROP 2 | PROP 3 |
| --- | --- | --- | --- | --- | --- |
|  | A neg |  | 3,2667 | 3,2667 | 2,9 |
|  | A pos |  | 17,633 | 18,267 | 17,3 |
|  | A tot |  | 20,9 | 21,533 | 20,2 |
|  | x-centroid of A neg |  | -0,159 | -0,157 | -0,159 |
|  | x-centroid of A pos |  | 0,5588 | 0,5599 | 0,5595 |
| No of neg.constr |  |  | 49 | 48 | 48 |
|  | MIN g |  | -0,478 | -0,459 | -0,687 |
| Relative Adequacy Index |  |  | 0,8437 | 0,8483 | 0,8564 |
| Preference (suggestion) |  |  | 3 | 1 | 2 |

DIAGRAM 3 : Histogram of normalized safety factors for all strakes of double bottom structure