Comparison of observed and calculated excess water (drainage discharge) in drained soil

Šimunić I.1, F.Tomić1, T. M. Minkina2, V. P. Kalinitchenko2, M. Vukelić-Shutoska3,

V. Filipović1, M. Bubalo1

1University of Zagreb, Faculty of Agriculture, Department of Soil Amelioration, Zagreb, Croatia

2Faculty of Biology and Soil Science, Department of Soil Science, Southern Federal University, Rostov-on-Don, Russia

3Institute of Environment, Faculty of Agricultural Sciences and Food

Ss. Cyril and Methodius University, Skopje, Republic of Macedonia

E-mail: simunic@agr.hr

Abstract

The research objective was to determine, in the period from September 2009 to August 2010, excess water (drainage discharge) in drained soil, type Gleyic Podzoluvisol, at different drainpipe spacings (15 m, 20 m, 25 m and 30 m, with contact material gravel and average depth of 1 m) and to compare it with excess water in soil mathematically calculated by the Thornthwaite and Palmer methods. The total amount of precipitation in the mentioned period was 1159.5 mm.

Excess water measured with limnigraphs and amounted to 350 mm at drainpipe spacing of 15 m, 340 mm at 20 m spacing, 328 mm at 25 m spacing, and 320 mm at 30 m spacing. Excess water in soil calculated by the Thornthwaite method was 424.4 mm and by the Palmer method 404.2 mm.

The obtained results clearly show that there are differences both between the tested drainpipe spacings and between the results calculated by the Thornthwaite method and the Palmer method. Measured data at all drainpipe spacings were smaller than mathematically calculated by both methods.

Measured and calculated excess water in drained soil depends on the total amount of precipitation, its distribution, drainpipe spacings, crop type and the mathematical method used.

Location of experimental drainage field

Drained soil, type Gleyic Podzoluvisol

Major characteristics of drained Gleyic Podzoluvisol

| Horizon | Depth (cm) | Silt (%) | Clay (%) | P (vol. %) | Cw (vol.%) | Ca (vol.%) | φv (g.cm-3) | φs (g.cm-3) | c (m.dan-1) | pH MKCl | Humus (%) | P2O5 | K2O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  |  | mg.100 g soil-1 |
| Ap | 0-35 | 51 | 48 | 49 | 48 | 1 | 1,32 | 2,58 | 0,14 | 4,7 | 4,1 | 9,7 | 19,2 |
| Gr | 35-45 | 58 | 41 | 48 | 47 | 1 | 1,34 | 2,57 | 0,06 | 5,0 | 1,3 | 1,4 | 8,8 |
| Gr/so | 45-90 | 63 | 36 | 43 | 42 | 1 | 1,52 | 2,66 | 0,07 | 5,9 | 0,7 | 2,9 | 7,9 |
| Gso/Gr | 90-115 | 73 | 23 |  |  |  |  |  |  |  |  |  |  |
| Gr | 115-130 | 76 | 20 |  |  |  |  |  |  |  |  |  |  |

Interpretation of signs: P- porosity, Cw- capacity of water, Ca-capacity of air, φv-bulk density, φs-specific density, c-coefficient of permeability

Precipitation during the investigation period (mm), Meteorological station Sisak

| 2009 | 2010 | Total (mm) |
| --- | --- | --- |
| IX | X | XI | XII | I | II | III | IV | V | VI | VII | VIII |  |
| 30,2 | 88,4 | 102,2 | 94,8 | 105,4 | 88,6 | 66,3 | 59,0 | 156,9 | 146,2 | 64,9 | 156,6 | 1159,5 |

Monthly and total drainage discharge at different drainpipe spacings (mm)

| Drainpipe spacing (m) | 2009 | 2010 | Total (mm) |
| --- | --- | --- | --- |
|  | IX | X | XI | XII | I | II | III | IV | V | VI | VII | VIII |  |
| 15 |  |  | 25 | 63 | 67 | 56 | 28 | 5 | 33 | 47 |  | 26 | 350 |
| 20 |  |  | 23 | 62 | 65 | 55 | 28 | 5 | 32 | 47 |  | 23 | 340 |
| 25 |  |  | 20 | 60 | 62 | 52 | 25 | 4 | 32 | 47 |  | 26 | 328 |
| 30 |  |  | 20 | 59 | 60 | 52 | 25 | 4 | 31 | 46 |  | 23 | 320 |

Balance of water in  soil, according Thornthwaite,s

| Year | 2009 | 2010 | Total |
| --- | --- | --- | --- |
| Month | IX | X | XI | XII | I | II | III | IV | V | VI | VII | VIII |  |
| Potencially evapotranspiration (corrected)-PETc (mm) | 86,6 | 41,8 | 23,6 | 6,8 | 0,0 | 3,1 | 25,7 | 57,0 | 95,5 | 129,9 | 156,4 | 124,2 | 750,6 |
| Precipitation (mm) | 30,2 | 88,4 | 102,2 | 94,8 | 105,4 | 88,6 | 66,3 | 59,0 | 156,9 | 146,2 | 64,9 | 156,6 | 1159,5 |
| Reserve of water in soil (mm) | 0 | 46,6 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 8,5 | 40,9 |  |
| Actually evapotranspiration-AE (mm) | 30,2 | 41,8 | 23,6 | 6,8 | 0,0 | 3,1 | 25,7 | 57,0 | 95,5 | 129,9 | 156,4 | 124,2 | 694,2 |
| Excess of water in soil (mm) | 0 | 0 | 25,2 | 88,0 | 105,4 | 85,5 | 40,6 | 2,0 | 61,4 | 16,3 | 0 | 0 | 424,4 |
| Deficit of water in soil (mm) | 56,4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 56,4 |

Balance of water in soil, according Palmer,s

Crop: Oilseed rape

Soil: clayey-loamy texture

Depth: 30 cm

| Month | Peff. | ETo/ETc | L 1 | L 2 | F | D | AE | Reserve of water in soil | ET-AE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | R1 | R2 | R=R1+R2 |  |
|  | mm | mm | mm | mm | mm | mm | mm | mm | mm | mm | mm |
| I | 87,6 | 2 | 0,0 | 0,0 | 0,0 | 85,4 | 2,2 | 43,0 | 86,0 | 129,0 | 0,0 |
| II | 76,0 | 6 | 0,0 | 0,0 | 0,0 | 70,1 | 5,9 | 43,0 | 86,0 | 129,0 | 0,0 |
| III | 59,3 | 28 | 0,0 | 0,0 | 0,0 | 31,4 | 27,9 | 43,0 | 86,0 | 129,0 | 0,0 |
| IV | 53,4 | 72 | 19,1 | 0,0 | 0,0 | 0,0 | 72,5 | 24,0 | 86,0 | 110,0 | 0,0 |
| V | 117,5 | 98 | 0,0 | 0,0 | 19,1 | 0,8 | 97,7 | 43,0 | 86,0 | 129,0 | 0,0 |
| VI | 112,0 | 48 | 0,0 | 0,0 | 0,0 | 64,0 | 48,0 | 43,0 | 86,0 | 129,0 | 0,0 |
| VII | 58,2 | 140 | 43,0 | 25,5 | 0,0 | 0,0 | 126,7 | 0,0 | 60,5 | 60,5 | 10,5 |
| VIII | 117,4 | 112 | 0,0 | 0,0 | 5,8 | 0,0 | 111,6 | 5,8 | 60,5 | 66,3 | 0,0 |
| IX | 28,7 | 26 | 0,0 | 0,0 | 2,5 | 0,0 | 26,3 | 8,3 | 60,5 | 68,7 | 0,0 |
| X | 75,9 | 16 | 0,0 | 0,0 | 59,6 | 0,0 | 16,3 | 43,0 | 85,3 | 128,3 | 0,0 |
| XI | 85,5 | 7 | 0,0 | 0,0 | 0,7 | 77,5 | 7,4 | 43,0 | 86,0 | 129,0 | 0,0 |
| XII | 80,4 | 5 | 0,0 | 0,0 | 0,0 | 75,0 | 5,4 | 43,0 | 86,0 | 129,0 | 0,0 |
| Yearly | 952 | 560 | 62 | 26 | 88 | 404 | 548 |  |  |  | 10,5 |
| In vegetation | 487 | 495 | 62 | 26 | 27 | 65 | 483 |  |  |  | 10,5 |
| Out of veget. | 465 | 65 | 0 | 0 | 60 | 339 | 65 |  |  |  | 0,0 |
| *Source: Palmer W. C., 1965: corrected: Vidaček Ž., 1981 |  |  |  |  |
| Interpretation of signs: | Peff. = Effective precipitation | D = Drainage of excess water |
|  | ETo = Reference evapotranspiration | AE = Actually evapotranspiration |
|  | ETc = Culture evapotranspiration | R1 = Reserve of water in surface layer (10 cm) |
|  | L1 = Loss of water from surface layer (10 cm) | R2 = Reserve of water in surface layer |
|  | L2 = Loss of water from subsurface layer | PAW = Physiologic active water |
|  | F = Fill of soil with precipitation | ET-AE = Deficit of water |