Analysis of Woven Fabrics for Men's Suit

Darko Ujević, Stana Kovačević, Jacqueline Domjanić

Faculty of Textile Technology, University of Zagreb, Zagreb 10000, Croatia

*Corresponding author’s email: Jacqueline Domjanić Jacqueline.domjanic@ttf.hr

(*This email address will be shown up in proceedings only)

Presenting author’s email address:

1st author’s email address: darko.ujevic@ttf.hr

Abstract The paper describes the design and analysis of woven fabrics for manufacturing of men's business suit. Three woven fabrics made of a blend wool/polyester with similar construction parameters and the fourth with an addition of 2% elastane fibers were designed. Physical and mechanical properties as well as the range of objective evaluation using the FAST system (Fabric Assurance by Simple Testing) including a complex procedure of assessing fabric quality were tested. Although some samples are made of the same raw material and fineness, woven in the same weave, with a slightly different density and different dyes and weight, the tested parameters differ. The plain-weave fabrics with a higher density and weight have a smaller thickness than those woven in twill weave and with a lower density or weight. Surface thickness is greater in the samples with less weight containing single yarn in the warp and weft and a portion of elastane fibers. Released thickness is usually smaller in the samples woven in plain weave than those woven in twill weave, regardless of the elastane in the fabric. Shorter bending length is present if the sample has a portion of elastane, as well as in twill-weave samples in relation to plain-weave samples without elastane. Greater fabric elongation will be present with elastane in the plain-weave fabric. Greater ability of design and dimensional stability can be achieved in plain-weave fabrics in relation to twill-weave. Keywords: woven fabrics, physical and mechanical fabric properties, Men's suit

1. Introduction

Apparel manufacturing process involves processing steps with the purpose to achieve the fulfilment of a finished clothing product. Woven fabrics are the raw material in the clothing manufacturing process where the material is transformed into an apparel product using 2D block pattern of cloth surfaces. Understanding of fabric properties is indispensable for the production of quality products. Textile materials (fibers, yarns and fabrics) are in the process of manufacturing and later during use they are stressed in various ways as: compressive, tensile, shear, bending and torsion. The methods of these loads have been relatively little explored, although they are of great importance when using the fabric [1-3].

This paper discusses the newly designed woven fabrics which will be used men's suit, where apart from the physico-mechanical properties,  the area of objective evaluation  using the FAST system  by means of the complex assessment procedure of fabric quality will be analyzed.

2. Experimental Part

Four different samples of the fabric for making men's suit. Objecitve evaluation and physical-mechanical fabric properties were tested and qualitative properties of each fabric were given. Prior to testing the samples were left in standard conditions (realtive humidity 65±2% and temperature 20 ± 2°C) which ensured the reproducibility of results. The basic fabric parameters such as mechanical fabric properties were tested on the Statimat M tensile tester made by Textechno in accordance with the standard  EN ISO 1421:1998.

  - The FAST system

The investigation of the area of objective evaluation and of the complex process of the assessment of fabric quality is possible only with well-equipped measuring devices. The FAST system measures fabric mechanical properties at low-stress level loads, which respond to real wearing conditions. These instruments are designed to be used by tailors and manufacturing plants to show durability of fabrics. They are simple to use and determine the deformation rate and can also show the behaviour of fabrics during production and wearing [4,5].

The FAST system consists of four measuring instruments: FAST-1 measuring instrument for measuring compressibility, FAST-2  instrument for measuirng bending properties, FAST-3 instrument measures fabric extensibility at low loads and FAST-4  is a quick test for measuirng fabric dimensional stability, including both relaxation shrinkage and expansion. The tested values are stored, and on the basis of these data the impact of individual fabaric properties in clothing manufacturing can be determined [6-8].

3. Results

Fabric samples I, II and III were woven from the same raw material (45% wool, 55% polyester) with the same yarn count (25x2). Samples I, II and IV were woven in plain weava, and sample III was woven in twill weave 2/2. The differences between samples I and II is insignificant in yarn density (sample I: 18.7/17.6 threads/1cm; sample  II: 19.6/18,7 threads/1cm) and in fabric weight (sample I: 318 g/m2; sample II: 326 g/m2) (Fig. 2). Sample III woven in twill weave   has a slightly higher thread density  in the first two samples (28/22 threads/1 cm) and weight (355 g/m2). Sample IV has a different raw material composition than the previous three samples (44% wool, 54% polyester and 2% elastane fibre), yarn fineness (33 tex) and fabric weight (195 g/m2). The fabric was woven in plain weave as the first two samples. Since samples I and II do not differ in the yarn type and fineness  with smaller deviations in  density and weight, the breaking force does not differ much (warp: 714.2/729.7 N, weft: 609.6/611.2 N), as well as the elongation at break  (warp: 31.7/36.9%, weft: 30.1/31.2%). Sample III with the same yarn as samples I and II, but a higher density and woven in twill weave has a higher breaking force than the first two samples (warp: 1100.1 N, weft: 853.4 N), as well as the elongation at break (warp: 51.5%, weft: 46.6%). Sample IV differing in raw material, fineness and density than the previous three samples has the lowest breaking force (warp: 509.9 N, weft: 438.4 N), but the elongation at break in the weft direction is greater (warp: 29.4%, weft: 45,6%) contributed by the elastane fibers in the yarn.

Figures  1-5 show the test results of the FAST system.

Fig. 1. Thickness and surface thickness by fabric samples

Fig. 2.  Bending length and bending rigidity

Fig. 3. Extensibility properties in the warp and weft direction by samples

Fig. 4.  Formability by fabric samples

Fig. 5. Relaxation shrinkage and hygral expansion in the warp and weft direction

4. Conclusion

Fabrics for making men's suits are mostly made of a woll/polyester blend, and in case of light-weight and finer dresses a lower percentage of elastane fibers is added. Fabrics are mostly woven in plain or twill weave 2/2.

In addition to construction parameters and raw material, it is also essential to evaluate the quality based on objective evaluation. The objective evaluation of fabric quality was enabled only after the development of new equipment because human influence is now excluded. Textile care procedures for these fabrics can be exactly investigated, and changes during use can be planned. This way it is possible to design fabrics with optimal properties. The optimization of manufacturing fabrics for men's suits and its further design into 3D shape can be largely facilitated using parameters measured in the FAST system.  The test results of objective evaluation depend on fabric construction parameters and raw material to a great extent.

The fabrics woven in plain weave with greater density and weight are less thick than those woven in twill weave and with less density and weight. Surface thickness is greater in fabrics woven from single yarns, in twill weav and fabrics containing elastane. Relaxed thickness depends on measurement loads; however, plain-weave fabrics always have less thickness than twill weave and the fabrics containing elastane. Relaxed thickness is lower in fabric samples woven in plain weave than in those woven in twill weave, regardless of elastane contained in the fabric.

Bending length also depends on weave and raw material and does not differ much in the warp and weft direction if density, raw material and fineness are the same. If a shorter bending length is necessary, the sample containing elastane will be more favourable as well as twill weave in contrast to plain weave.

Bending rigidity increases by weaving in plain weave. The fabric woven in twill weave has less bending rigidity than the fabric containing elastane draws the attention to the fact that weave plays a dominant role in bending rigidity, followed by raw material and fabric color.

Greater fabric extensibility will be achieved using elastane in the fabric and by weaving in plain weave.

Greater formability as well as dimensional stability can be achieved in plain-weave fabrics rather than in twill-weave fabrics. Greater hygral expansion is achieved in the sample containing elastane in contrast to other samples.

Taking account of the conclusions drawn on the basis of physical and mechanical properties and by measuring in the FAST system with a complex procedure of evaluating fabric quality, it is possible to design a fabric with desirable properties for men's suit relatively precisely.

5. Acknowledgement

This research was realized in part through a grant by the manufacturing plant Varteks d.d. The authors express their gratitude to Dr. Jelka Geršak and Dr. Andreja Rudolf from the University of Maribor for their help and efforts completing this research.

The results shown in the paper resulted from the scientific program (Advanced Technical Textiles and Processes, code: 117-0000000-1376 and Anthropometric Measurements and Adaptation of Garment Size System, code: 117-1171879-1887) conducted with the support of the Ministry of Science, Education and Sports of the Republic of Croatia.

References

- Geršak J. Design and clothing manufacturing processes. A systematic approach to planning, scheduling and control. Woodhead Publishing Limited, 2013.

- Domjanić Ž, Kovačević S, Geršak J, Ujević D. Analysis of the fabrics for the manufacture of formal Academic Gowns, 11th World Textile Conference AUTEX 2011, Book of Proceedings, Volume 1, 150 Years of Research and Innovation in Textile Science, Adolphe Dominique C., Schacher Laurence (ur.), Mulhouse, Ecole nationale Supérieure d´ Ingénieurs Sud-Alace, 2011. 119-122.

- Kovačević S., Gordoš D. Impact the Level of Yarn Twist on Sized Yarn Properties, Fibres & textiles in Easten Europe, 2009:17;6:44-49.

- Ancutiene K, Strazdiene E, Nesterova A. The Relationship between Fabrics Bending Rigidity Parameters Defined by KES-F and FAST Equipment. Proceedings of the Estonian Academy of Sciences, 2012;61:3:150-159.

- Ly NG. Simple Instruments for Quality Control by Finishers and Tailors. Textile Research Journal: 2011:81:6.

- Geršak J. Objektivno vrednovanje fiksiranih dijelova odjeće. Tekstil: 1997; 46:4:193-203.

- Hursa A. et al. FAST mjerni sustav za objektivno vrednovanje mehaničkih i fizikalnih svojstava tkanina. Tekstil; 1998:47;8:401-408.

- Zavec Pavlinić D, Geršak J. Vrednovanje kakvoće izgleda odjeće. Tekstil: 1997;46:4:193-203.