## Slide 1
Goran Jurković, M.Sc., and Edouard Ivanjko, Ph.D.
Faculty of Transport and Traffic Sciences, University of Zagreb, Croatia, www.fpz.hr
Vlado Sruk, Ph.D.,
Faculty of Electrical Engineering and Computing, University of Zagreb, Croatia, www.fer.hr
Application of GNSS Technology for Car Tracking and Remote Control

## Slide 2: Introduction
Research conducted in usage of GNSS Technology in real world scenario to make everyday car using more user friendly and to further increase car safety (grand theft auto)
Car monitoring (tracking and engine history) and remote controlling (doors, locks, windows, engine start and shut down)
Achieved solution based on integration of technologies: GSM, GPRS, GPS/GNSS, CANBUS, LAMP (HTML, PHP, MySQL), TCP/Ip socket server, Android Application
Notes: Research conducted in usage of GNSS Technology in real world scenario to make everyday car using more user friendly and to further increase car safety (grand theft auto)
Car monitoring (tracking and engine history) and remote controlling (doors, locks, windows, engine start and shut down)
Achieved solution based on integration of technologies: GSM, GPRS, GPS/GNSS, CANBUS, LAMP (HTML, PHP, MySQL), TCP/Ip socket server, Android Application

## Slide 3: Introduction – Car Safety
Widely available after market alarm systems:
  one way or two way remote controllers
  limited distance
  additional gadgets to carry in pockets
Standard in-fabric alarm systems:
  basic options
  easily disabled by thefts
All lack of tracking history and monitoring information
Notes: Prikazi tmonkey6

## Slide 4: Introduction – Car Safety of Future
GNSS/GPRS Based Device:
  Integration of many services (remote control, tracking, etc)
  Limitless distance of remote control
  Tracking and car monitoring history
  No need for carrying car keys or additional gadgets
Notes: Prikazi MOTOcommanderEN

## Slide 5: Introduction – Achieved solution
Remote control of the vehicle:
  Engine start up and forced shut down
  Door locks and alarm control
  Window opening and closing
  Car monitoring and information about theft actions
  No need for carrying car keys
Tracking history and additional engine information:
  engine rpm and car speed
  trip history and current location
Additional keyless car entry in emergency:
  unlocking the car with entering PIN on hidden keyboard button

## Slide 6: Introduction – Achieved solution
Remote control and monitoring of the vehicle over:
  GUI on application for smartphone
  text UI interface over messages (SMS) for older phones
  GUI on Web page on personal computer

## Slide 7: Introduction – Achieved solution
Advancement in technology using GNSS device

## Slide 8: GNSS capable device inside Vehicle
Hardware based on Atmel AVR micro-controller and SimCom Ltd. SIM908 GSM/GPRS/GNSS module
Device is equipped with FOTA for faster development of a software inside by enabling firmware updates over the GPRS using HTTP
On board alarm features and sensors
Interface to car engine and harness
MCP2515 CANBUS processor and MCP2551 driver for addition information on newer cars
Smaller version in waterproof casing for motorcycle installation

## Slide 9: Wiring device to Vehicle ECU

## Slide 10: CANBUS connection to Vehicle ECU
Hardware based on Mocrochip MCP2515 and MCP2551
Information about vehicle state over just two digital wires
Every car model has it’s own addresses of particular information (big database of every car make and model)
Possibility of sending commands over CANBUS to change particular state of the car:
  locking and unlocking doors
  opening and closing windows
  turning lights on and off
  starting up the engine
Information about CANBUS addresses about particular car is proprietary information and cannot be obtained by legal channels (reverse engineering)

## Slide 11: Wiring configuration of Device

## Slide 12: Linux based Main server
TCP/Ip statefull socket server (GCC)
  Permanent TCP connection to vehicle and Android devices
  Relaying commands from Android devices to vehicle
  Relaying and sending SMS on alerts
  Stores geo location and other data in MySQL database for history and reports
HTTP server based on PHP
  Generating and displaying tracking history and vehicle information
  Complex setup of geofences, personnel, vehicle rules and policies

## Slide 13: HTTP server based on PHP

## Slide 14: Android Application as a Remote Controller
Remote controller based on graphical user interface (work in progress)
Doesn’t have distance limitation (GSM coverage)
Permanent TCP/Ip connection to socket server for faster command relay (relaying time under 1 second)
Additional information and future upgrades available with simple change of the application
Displayed buttons correlate to real in-car installation
Notes: prikazi vovlolunl i audi a5

## Slide 15: Conclusion and future work
GUI for Android and IPhone applications needs attention
expanding CANBUS database is constant work in progress
solving sending CANBUS commands to car’s ECU would make installation easier and more market friendly
  less installation working hours (possibility of marketing outside of Croatia)
  installation could be done by amateurs (cost of installation lowered)
more complex traction history and additional reports are work in progress

## Slide 16: Thank you for attention!
For further information, please contact:
  goran.jurkovic@fpz.hr
  edouard.ivanjko@fpz.hr
  vlado.sruk@fer.hr
  http://www.globis.hr/